Building and Deploying a Curved Screen

Design the Screen

Fly Elise design

Buy the Screen

South Korean screen company

NOTE THERE MAY BE AN ERROR IN THE SCREENSHOTS I MISSED SAVING THE WORKING SETTINGS FROM SUNDAY ARRRGGHHHHH

Align the Screen

In windows group the three projectors together using Surround view
Fly Elise Calibration Pro (which needs Fly Elise Ultimate Version
start the Client – and then the Server.
In the Server select the projectors, best to do one by one to ensure you have them in the right order (3x1)
Set screen size of 40 * 10

Place Dots on the Screen

Once the Squares are good

Then Calculate frustrion
Export both Procalbllib and enable DCS (needs two check boxes)

Copy the exported files from the Fly Elise Calibration Pro to c:\wrap000) you are allowed to use folders and the Monitor.lua file to My Saved Games\DCS]Config\Monitor

In Fly Elise Pro

Set and remember the Desktop and Window Warp files. It looks like Fly Elise goes looking for the execution of specific executables to determine if warping is needed or not

I found display both the warped and warped cursor was useful
Import the hardware Cabliration file that was copied to c:\warp000
Use the Multi-projector calibration fie
Select Games DCS and Specify the folder in Saved Games – it only goes looking for monitor.lua

In DCS – do not use Full screen, Set the Screen resolution to cover all screens – select the Monitor.lua file.
While doing initial trouble shooting you may want to select one screen