# Purpose

This document covers the design overview and build steps for the Hornet.

# Acknowledgements

The Hornet was built following early Beta Open Hornet designs. The Open Hornet project is nothing short of amazing, with full 3D cad models and electronic designs. Full credit to John (Noctum) and the team for delivering a truly open set of plans for the Hornet.

The bulk of communications occur on Discord.
https://discord.com/invite/G5PA5ju
https://openhornet.com/
https://github.com/jrsteensen/OpenHornet

The electronics used in this pit aren’t based on the Open Hornet stack as they Open Hornet stack wasn’t available at the beginning of the build.

Ben and Luke have been a big part of the team in building the Hornet in Oz. Thanks gents.

# Systems Overview

The Hornet currently supports DCS and MSFS 2020. DCS provides full system capabilities, whilst MSFS 2020 supports a basic aircraft tooling. The bulk of the interfacing with DCS uses the Flight Panels fork of DCS-BIOS. Further details on API usage and development can be found in Python HW Link - Design

The throttle and stick assembly are from WinWing (https://www.winwing.cn/en/JOYSTICK) and the rudder pedals are from MFG (https://mfg-sim.com/en/).

As the ADI is not natively rendered in DCS, Helios is used to generate the ADI. The Left and right DDIs along with the AMPCD can be easily exported, but views such the RWR/TEWS, do require a little more work to export.
# Systems Design Approach

# Component Details

### Panel Backlighting

The Panels are driven by a hardware solution developed by Luke. It uses PCBs with SMD (Surface Mounted) LEDs, which enable knobs to be effectively backlit, something that is difficult when using through hole LEDs.
The LEDs used are from the NeoPixel family, who do not have a separate clocking or data load pin. This has the major benefit of enabling 100’s of LEDs to be driven with a four wire interface (Power, Ground, Data-In, Data-Out). It does however introduce a timing consideration, the LEDs expect a constant data feed when updating, i.e. the Arduino library (FastLED) should not be interrupted when doing an update. If it is interrupted all sorts of strange colours and state is encountered, often toward the end of the led chain. As the Arduino DCS-BIOS library uses interrupts to receive serial data over the USB interface, and most Arduino CPUs are only single threaded the DCS-BIOS and FastLED are not good neighbours with long LED chains.
This challenge was solved by splitting DCS-BIOS and the FastLED library onto two Arduino’s with the DCS-BIOS Arduino sending lighting updates over Ethernet to the FastLED library.
Some devices are backlight using PWM, this includes some of the first generation of gauges. Later gauges (eg Standby Instruments) using the NeoPixel LEDs.
The backlighting levels are derived from DCS-BIOS, the Flight Panels fork presents these values, whereas the original DCS-BIOS does not.
A design note when using ground and power planes with PCBs, Thermal Reliefs should be included as this reduces the amount of heat needed to solder or remove a device. For reference - https://resources.pcb.cadence.com/blog/2021-pcb-thermal-relief-guidelines-for-effective-layouts.

The 5mm NeoPixel LEDs used in the Standby instruments use a different colour encoding, From (https://www.adafruit.com/product/1938), ‘These are "RGB" instead of "GRB" format used in the 5050-sized LEDs you are so used to’.
### Rudder Pedals
The pedals are MFG Crosswinds, and are beautifully engineered. The optional Damper is well worth the investment. The footrests aren’t from MFG, at the time of purchase, a team on the DCS forums was manufacturing F-16 footrests (https://forum.dcs.world/topic/256148-mfg-crosswind-f-16-combat-pedals/)

The pedals are mounted on a plate driven by a motor, enabling the pedals to be adjusted using a switch in the forward lower panel assembly. Limit switches are used. The plate is mounted on a pair of rails.

### Throttle Assembly
As the WinWing throttle was not part of the original Open Hornet design the panels to the left and forward of the throttle required modification.
The throttle was removed from its outer enclosure, and the backlighting was modified, in that is not longer driven by the WinWing electronics, but instead is driven by the custom PWM (Pulse Width Modulation) dimmer. Additional resistors were added to allow the LEDs to be driven by 12V.

# Computer Specifications

The following capabilities are desired
- Dual Wired Ethernet Interfaces, one for the Arduinos, the other for high performance connectivity such as last software updates and over the wire backups.
- WiFi interface for general connectivity
- Sound card with front and rear ports
- Six USB Ports
- Removable SSDs to facilitate high performance backups and swapping of simulator personalities (eg swap between DCS A10 and F16)
- Three high performance HDMI interfaces for the primary screens
- Ideally an HDMI port for the operators screens
- Four HDMI ports for the DDIs, AMPCD, and the standby ADI and RWR.
- An additional three video ports for the mirrors.

## Video Sub-system

With a minimum eight video ports there are some challenges in meeting these requirements. If mirrors are desired, a total of 11 ports are needed.
The original PC had a Nvidia 2080TI and a smaller three port Nvidia.
Ben found a four Port USB-3 video card which provides solid performance for DDIs and AMPCDs. The Startech USB32HD4 USB 3.0 to 4 HDMI Adapter - Quad Monitor lands around AU$270.
## 2023 Computer Specification
The PC was originally running a Nvidia 2080, it is intended to refresh the PC with a higher specification video card as a number of Blue Screens had occurred leading to the original PC not being able to boot.
The replacement PC is this configuration.
- Intel S1700 Core i9 13900K 24 Core CPU BX8071513900K
- Corsair iCUE H150i RGB ELITE Liquid CPU Cooler CW-9060060-WW
- MSI S1700 E-ATX MEG Z790 ACE DDR5 Motherboard
- 64GB DDR5 (2x32G) Corsair 5200MHz CMT64GX5M2B5200C40 Dominator Platinum RGB RAM
- Samsung 990 PRO PCIe 4.0 NVMe M.2 SSD 2TB - MZ-V9P2T0BW
- Nvidia Quadro T600 4GB PCIe Video Card 900-5G172-2520-000
- Gigabyte RX7900XTX 24GB PCIe Video Card GV-R79XTX-24GC-B
- Corsair Full ATX Obsidian 1000D Tempered Glass Case Black (No PSU) PN CC- 9011148-WW
- 120mm Noctua NF-A12x25 FLX 2000RPM Fan
- 1200 Watt Thermaltake Toughpower GF3 Gen5 Power Supply PS-TPD-1200FNFAGA-4
- Microsoft Windows 11 Home 64bit DVD KW9-00632

# Building the Computer

1. Install Operating System
2. Install Backup/Imaging Software (currently use Acronis True Image – but the perpetual licenses are no longer available – so may need to look for altnertauves

# Applying DCS Updates

It is common for DCS to update the LUA files associated with the TEW and one other of the outputs. A reasonable approach is to keeping a renamed copy of the master in the same directory and then copying it over the updated files.