Looks like different builds will need to be compiled to run P3d and MSFS, P3d for Dodo and MSFS for Flyinside and Cowan

Data returned as off 202601260757

Values wanted

Test with Generic MSFS Helicopter and then Dodo

When adding
Battery On	Cowan	Attribute
Avionics Power	Yes	Could also monitor bus voltage if so desired
Altitude	Yes	altitude
Radar Altitude	Yes	PLANE_ALT_ABOVE_GROUND
VSI	Yes	VERTICAL_SPEED
Airspeed	Yes	airspeed
Attitude Bank	Yes	ATTITUDE_INDICATOR_BANK_DEGREES
Attitude Pitch	Yes	ATTITUDE_INDICATOR_PITCH_DEGREES
EngineTorque	Yes	ENG_TORQUE_PERCENT_1
TransmissionPressure	No	Deprecated - ENG TRANSMISSION PRESSURE
TransmissionTemperature	No	Deprecated - ENG TRANSMISSION TEMPERATURE
EnginePressure	Yes	ENG OIL PRESSURE:1
EngineTemperature	Yes	ENG OIL TEMPERATURE:1
GasProducer	Yes	TURB_ENG_CORRECTED_N1_1
EGT
FuelPressure
ElectricalLoad	Yes	ELECTRICAL TOTAL LOAD AMPS
FuelLevel	Yes	FUEL TOTAL QUANTITY

TurbineSpeed	Yes	GENERAL_ENG_PCT_MAX_RPM_1
RotorSpeed	Yes	ROTOR_RPM_PCT_1

Working Values
- Gear Centre
- Gear Left
- Plane Heading True
- Absolute Time
Know Bad Values
Plane Heading Mag
Gear Right
- Possible Bad
- Outer Marker – behaves more like inner marker

Keystrokes
Ctl Space – toggle parking brakes
/ Toggle Landing gear
Snipping tool Windoes Key – Shift - S
For PCs running MSFS and using c# projects need to add the following to build instructions
Install Visual Studio
Install MSFS2024 SDK ideally to c:\msfs 2024 sdk as the absoulte path is referenced in the c# project

Both simconnect.dll and Micorsoft.MSFS.Simconnect.dll must be added to the project.
Using Visual Studio
1. Add the file to the project:
  1. In Solution Explorer, right-click the project name or the folder where you want to add the file.
  2. Select Add > Existing Item....
  3. Browse to the file's location, select the file, and click Add.
2. Set file properties:
  1. Select the file in Solution Explorer.
  2. Open the Properties window (press Alt+Enter or right-click the file and select Properties).
  3. In the Properties window, change the Build Action to Content (or another appropriate action, like None, depending on your use case).
  4. Change the Copy to Output Directory setting to either Copy Always or Copy if Newer (the latter is generally preferred to avoid unnecessary rebuilds).

Key Differences in C# SimConnect:
1. Direct SDK Usage: Instead of a Python wrapper, we'll use the Microsoft.FlightSimulator.SimConnect.dll directly.
2. Event-Driven: SimConnect in C# is heavily event-driven. You register handlers for events like connection, disconnection, and data reception.
3. Data Definitions (Structs): You explicitly define C# structs to tell SimConnect how to package the requested data. For many individual variables, we'll request them one by one and collect them into a dictionary.
4. Message Loop: A SimConnect object typically runs in its own message loop or requires SimConnect.ReceiveMessage() to be called periodically. For a console app, we'll use a Timer to manage reconnection and a separate Timer for UDP sending.
5. UDP Client: System.Net.Sockets.UdpClient is used for UDP communication.
6. JSON Serialization: System.Text.Json (or Newtonsoft.Json) is used to serialize the collected data into a JSON string.
To make this C# code runnable:
1. Create a New C# Console Application Project in Visual Studio.
2. Add SimConnect Reference:
  1. Right-click on your project in Solution Explorer -> "Add" -> "Project Reference...".
  2. Browse to the location of Microsoft.FlightSimulator.SimConnect.dll. This DLL is part of the Microsoft Flight Simulator SDK. You'll typically find it in a path like C:\MSFS SDK\SimConnect SDK\lib\Microsoft.FlightSimulator.SimConnect.dll. If you don't have the SDK, you'll need to install it or locate this DLL from your MSFS installation (though the SDK version is preferred for development). NOTE THIS IS NOT A REFERENCE TO THE SIMCONNECT.DLL BUT THE UNDER ..\LIB\MANAGED

If you select the simconnect.dll itself

Aslo need to update project propoerties to copy simconnect.dll from the SDK to the output directory.

<Project Sdk="Microsoft.NET.Sdk">

  <PropertyGroup>
    <OutputType>Exe</OutputType>
    <TargetFramework>net10.0</TargetFramework>
    <ImplicitUsings>enable</ImplicitUsings>
    <Nullable>enable</Nullable>
    <Platforms>x64</Platforms>
<PlatformTarget>x64</PlatformTarget>
  </PropertyGroup>

  <ItemGroup>
    <Reference Include="Microsoft.FlightSimulator.SimConnect">
      <HintPath>C:\MSFS 2024 SDK\SimConnect SDK\lib\managed\Microsoft.FlightSimulator.SimConnect.dll</HintPath>
    </Reference>
  </ItemGroup>

  <ItemGroup>
  <None Include="C:\MSFS 2024 SDK\SimConnect SDK\lib\SimConnect.dll">
    <CopyToOutputDirectory>PreserveNewest</CopyToOutputDirectory>
  </None>
</ItemGroup>

</Project>

1. Add System.Text.Json: This is usually included in modern .NET projects. If not, add it as a NuGet package.
2. Copy and Paste the Code: Replace the contents of Program.cs with the provided C# code.
3. Adjust UDP IP/Port: Ensure UdpIp and UdpPort match your Python UDP listener or Arduino receiver.
4. Build and Run: Build the project, then run it.