Building and Deploying a Curved Screen

Design the Screen

Fly Elise design

Buy the Screen (South Korean)

Setting up with ATI Card

Install Github Desktop and clone the Repo. This should be used to save the configuration settings.

Download and install Calibration Pro. It installed in the Downloads Directory.
Disable the Windows Firewall (this may not be necessary)
Run the INSTALL_FIRST_BONJOUR batch file, without this the Server will not find the client.

Ensure all Projectors are running at desired resolution. Found the 4K 60Hz is very demanding on cabling – stuff you’d get away with for 1080 just doesn’t work.

As there is temperature induced picture drift – run the projectors and air conditioning (22C) for an hour to allow things to stablise.

Check all three projectrs are correctly listed in Windows Display Settings. Have had issue where the Projectors ‘fell off’ the PC when incorrectly setting using Nvida instead of ATI warping, ultimately decided to run with Windows Warping. The impact was it disabled the projectors in Windowss

Group Displays Together

There are references to only allow a maximum on 1 HMDI port within an Eyefinity Group. Currently running a Display Port, USB-C port and HDMI port.

AMD Software
- Display. There should be three displays listed.
- Scroll down to the bottom and Select Eyefinity, Combine multiple displays to act as one.
- The software will then attempt to group the displays. The displays can be arranged after they have been grouped.

Start the Calibration Pro Client. Assuming a 1080 monitor is at the 0,0 screen position the grouped projectors should appear as a single box with
AMD Radeon RX7900 XTX
Generic PnP Monitor
Position 1920,0
Resolution 11520x2160
Projectors 3x1

Start the Calibration Pro Server. It should list the three projectors as used. If they are not present check the client can see them and Bonjour has been correctly configured on the PC. The project file is listed at the bottom of the screen and by default lives in the directory the program is install in – eg Downloads\Immervi..Pro_v5.1.1\Immervi..Pro_v5.1.1\. Change the project directory to the target directory in the Github Repo.

For my project this is .\Hornet Documentation\Fly Elise and then either 4K or 1080.
Once the screens are aligned explicitly set the save folder to the same directory. I’m exporting the following
- Procalib Warp & Blend
  - Single frustum (single.procalib)
  - (Perspective) Multi frustums (multi.procalib)
- Microsoft Flight Simulator
  - MSFS Multi-PC (single Projector per PC) [Experimental]
  - Was unable to select MSFS Single-PC (Multi-view) [Experimental]. Unsure why – currently running Calibration Pro 5.1.1
- DCS
  - DCS World (MonitorSetup.lua)

If creating a new project – after creating the new folder and saving the project, go to export and EXPLICITLY set the export folder – otherwise you’ll be stomping over the previous projects export.

Align the screen

The screen size used is 30x10.
Radius 2.000m, begin Vertical -0.8 End Vertical 1.6 Centre 0.8, Leg Length 1.0

Three Views

	Begin Column	Number of Columns	End Column (derived)
View 1	1	13	13
View 2	7	16	22
View 3	18	13	30

While Aligning ensure Automap is on and Continuous is on

Use the Shift-Arrow keys for Small movements, and the Ctrl-Arrow Large movements. Once you are happy with a view the grid can be locked to prevent accidental changes.

Operations

Firstly it appears you can’t have the best of both worlds (unless I’m missing the obvious) – to get a nice desktop warp and MSFS you need to use single procalib, but to get DCS to warp need multi.procalib.

When operating DCS don’t have Desktop warping or Windows warping enabled. Load DCS and start flight, once flight is loaded then enable windows warping. If performance has tanked, restart computer and repeat.

What is interesting the GUI tends to suggest separate calibration files can be used as it displays ‘External calib mutli.procalib’ and then the next line has ‘External calib desktop multi.procalib’

Using Two config sets -
Config Set 1 – Single.procalib – Desktop and MSFS – Shift-Ctl-1 to select – NEED TO VALIDATE THIS ISN”T COLIDING WITH DCS KEYSTROKES
Config Set 2 – Multi.procalib – DCS – Shift-Ctl-2 to select

As the default keystrokes clash with DCS settings, using Ctl-Z and Shift-Ctrl-Z. Also disabled all other keystroke options in FlyElise Pro.

In FlyElise Pro, in the Simulator integration screen select DCS, find the export folder from Calibration Pro (now living in the GitHub repo), and select the root directory for DCS (note two different DCS and DCS Open Beta.

Open DCS and select the Monitor file (Sim18….)

CMDNET is a simple TCP interface to Immersive Display Pro – default Port is

Fault finding with ATI Card

If you startThe Calibration Pro client and now projectors are present – it is possible the Eye Finity grouping has disappeared

Tried reducing the resolution to 1080 per projector, but when Eyefinity groups displays it sets them to 4K, and there doesn’t appear to be a way to reduce resolution once the displays are reduced

Need to determine if the merged projector displays can be used as Primary Display – it looks like they disconnect on restart

Align the Screen

In windows group the three projectors together using Surround view
Fly Elise Calibration Pro (which needs Fly Elise Ultimate Version
start the Client – and then the Server.
In the Server select the projectors, best to do one by one to ensure you have them in the right order (3x1)
Set screen size of 40 * 10

Place Dots on the Screen

Once the Squares are good

To reduce the size of blurry overlap make the slope vert steep

Then Calculate frustrion
Export both Procalbllib and enable DCS (needs two check boxes)

Copy the exported files from the Fly Elise Calibration Pro to c:\wrap000) you are allowed to use folders and the Monitor.lua file to My Saved Games\DCS]Config\Monitor

In Fly Elise Pro

Set and remember the Desktop and Window Warp files. It looks like Fly Elise goes looking for the execution of specific executables to determine if warping is needed or not

NOTE for DCS you need multi.procalib , but for MSFS you need single.procalib (at least when not using multiview)

I found display both the warped and warped cursor was useful
Import the hardware Cabliration file that was copied to c:\warp000
Use the Multi-projector calibration fie
Select Games DCS and Specify the folder in Saved Games – it only goes looking for monitor.lua

In DCS – do not use Full screen, Set the Screen resolution to cover all screens – select the Monitor.lua file.
While doing initial trouble shooting you may want to select one screen

MSFS Text File

Export for MultiPC (single channel per PC)
Locate the plane folder in the MSFS packages directory
Example: packages\Official\Steam\asobo-aircraft-c172sp-classic\SimObjects\Airplanes\Asobo_C172sp_classic
Locate and create a copy of the cameras.cfg
Locate the [CAMERADEFINITION.x] for Origin = "Virtual Cockpit"
Edit the camerss.cfg file and add/modify the InitialZoom and InitialPbh lines as indicated below

"C:\Users\bnepe\AppData\Local\Packages\Microsoft.FlightSimulator_8wekyb3d8bbwe\LocalCache\Packages\Official\OneStore\asobo-aircraft-b787-10\SimObjects\Airplanes\Asobo_B787_10\cameras.cfg"

------------------
Set the ZoomPercentage in MSFS GUI to 42.0656
Channel = 1
ProjectorName = Projector1
Enter the following values in the cameras.cfg file
InitialZoom = 1.0
InitialPbh = 9.8967, 0, -66.0839
------------------

------------------
Set the ZoomPercentage in MSFS GUI to 20.2342
Channel = 2
ProjectorName = Projector2
Enter the following values in the cameras.cfg file
InitialZoom = 1.0
InitialPbh = 9.75862, 0, -4.70305
------------------

------------------
Set the ZoomPercentage in MSFS GUI to 39.3367
Channel = 3
ProjectorName = Projector3
Enter the following values in the cameras.cfg file
InitialZoom = 1.0
InitialPbh = 12.1747, 0, 70.8311
------------------