# Purpose

This document covers the design overview and build steps for the Hornet.

# Acknowledgements

The Hornet was built following early Beta Open Hornet designs. The Open Hornet project is nothing short of amazing, with full 3D cad models and electronic designs. Full credit to John (Noctum) and the team for delivering a truly open set of plans for the Hornet.

The bulk of communications occur on Discord.
https://discord.com/invite/G5PA5ju
https://openhornet.com/
https://github.com/jrsteensen/OpenHornet

The electronics used in this pit aren’t based on the Open Hornet stack as they Open Hornet stack wasn’t available at the beginning of the build.

Ben and Luke have been a big part of the team in building the Hornet in Oz. Thanks gents.
# Systems Overview

The Hornet currently supports DCS and MSFS 2020. DCS provides full system capabilities, whilst MSFS 2020 supports a basic aircraft tooling. The bulk of the interfacing with DCS uses the Flight Panels fork of DCS-BIOS. Further details on API usage and development can be found in Python HW Link - Design

The throttle and stick assembly are from WinWing (https://www.winwing.cn/en/JOYSTICK) and the rudder pedals are from MFG (https://mfg-sim.com/en/).
# Systems Design Approach

# Component Details

### Panel Backlighting

The Panels are driven by a hardware solution developed by Luke. It uses PCBs with SMD (Surface Mounted) LEDs, which enable knobs to be effectively backlit, something that is difficult when using through hole LEDs.
The LEDs used are from the NeoPixel family, who do not have a separate clocking or data load pin. This has the major benefit of enabling 100’s of LEDs to be driven with a four wire interface (Power, Ground, Data-In, Data-Out). It does however introduce a timing consideration, the LEDs expect a constant data feed when updating, i.e. the Arduino library (FastLED) should not be interrupted when doing an update. If it is interrupted all sorts of strange colours and state is encountered, often toward the end of the led chain. As the Arduino DCS-BIOS library uses interrupts to receive serial data over the USB interface, and most Arduino CPUs are only single threaded the DCS-BIOS and FastLED are not good neighbours with long LED chains.
This challenge was solved by splitting DCS-BIOS and the FastLED library onto two Arduino’s with the DCS-BIOS Arduino sending lighting updates over Ethernet to the FastLED library.
Some devices are backlight using PWM, this includes some of the first generation of gauges. Later gauges (eg Standby Instruments) using the NeoPixel LEDs.
The backlighting levels are derived from DCS-BIOS, the Flight Panels fork presents these values, whereas the original DCS-BIOS does not.
A design note when using ground and power planes with PCBs, Thermal Reliefs should be included as this reduces the amount of heat needed to solder or remove a device. For reference - https://resources.pcb.cadence.com/blog/2021-pcb-thermal-relief-guidelines-for-effective-layouts.

The 5mm NeoPixel LEDs used in the Standby instruments use a different colour encoding, From (https://www.adafruit.com/product/1938), ‘These are "RGB" instead of "GRB" format used in the 5050-sized LEDs you are so used to’.
### Rudder Pedals
The pedals are MFG Crosswinds, and are beautifully engineered. The optional Damper is well worth the investment. The footrests aren’t from MFG, at the time of purchase, a team on the DCS forums was manufacturing F-16 footrests (https://forum.dcs.world/topic/256148-mfg-crosswind-f-16-combat-pedals/)

The pedals are mounted on a plate driven by a motor, enabling the pedals to be adjusted using a switch in the forward lower panel assembly. Limit switches are used. The plate is mounted on a pair of rails.

### Throttle Assembly
As the WinWing throttle was not part of the original Open Hornet design the panels to the left and forward of the throttle required modification.
The throttle was removed from its outer enclosure, and the backlighting was modified, in that is not longer driven by the WinWing electronics, but instead is driven by the custom PWM (Pulse Width Modulation) dimmer. Additional resistors were added to allow the LEDs to be driven by 12V.