Hornet Pit Assembly and Disassembly

# Disassembly

## Remove Skins
Remove screws from the bottom up, once on the top work from the edges towards the centre. Press against the skin to hold it in place while removing the last two screws.
Disconnect strobe and formation lights.
Figure 1: Port Rear Skin	Figure 2: Port Forward Skin
Figure 3: Starboard Rear Skin	Figure 4: Starboard Forward Skin

## Remove UIP Cover
Figure 5: UIP - Forward Section

Remove the two bolts for hud assembly, the AOA indicator is just sitting in its holder. Place AOA indicator forward shelf.
Place the port speaker on the forward shelf
Rotate the two positioning clips on the hud
Remove the bolts holding the cover, starting from the port side working towards the starboard side.
Remove port and starboard upper alignment plates

## Remove Canopy Bow
Unplug the connector to the GPS. / Remove the GPS. / Lift the cable glad to the Lock-Shoot and Bow Chart Light can be removed. / The cable path for the Lock-Shoot cable rises back into the LIP on the starboard side and traces directly to the LED distribution PCB.
The chart light follows a similar path to the Lock-Shoot, terminating on the PWM distribution pane.
The cable slack for the chart light lives in the LIP

Disconnect cables from the LED distribution board
Disconnect the Map Light cable from the PWM light distribution panel in the UIP
Disconnect the Compass cables
Unscrew the Canopy bow itself
Remove the canopy bow support brackets
## UIP
### Power Distribution Panel
## Disconnect Port/Left Console
Note there are nuts located midway along the bolt (between the console and UIP) that hold the bolt in place.

## Disconnect Cables
USB	Bone	Bone
Port Side PWM	Black	Green
Left console Flood left console
12V	Black	Red
Left Console Stepper Servos	White	Yellow
Left Console Digital Out	White	Red
Left Console	Black	Orange

## Disconnect Starboard/Right Console

Note the nuts sitting midway along bolts to hold the bolt in position

### Disconnect Cables
The cables stay attached to the console
Role	Cable Colour	Connector
Ethernet	Blue
Right Conn Power	Black
Strb Side Dimmer	Black	4 way Green
UFC Analog	White
Right Console LIP Servos	Black	6 way Yellow
Right Console LIP Digital	Back	6 way unpainted
Right Console LED	Black?	4 way Orange
Right Console LIP Stepper	Black
Dimmer Pots	Black	Blue
USB	Blue
12V	Black	Red
These could be left console
Something Power (utility light?)	Gray/Black	2 way unpainted
Ethernet	Blue
Backlighting	White	4 way Black
USB	Bone

## Remove Seat
Disconnect Cable and place it on seat cushion to prevent it becoming entangled. / Remove the port and starboard bolts which lock the extended support arms in place. / Remove the four screws (two forward, two aft) which attach the seat to the floor, an extension / shaft will make it easier to remove the two forward screws.
Unplug Stick USB connector. / Slid

### Disconnect Cable
### Remove Rear Support Cross Member
### Remove Seat Base Screws
Slide Seat Slightly back
### Remove Stick USB cable
### Lower seat rollers
### Slide Seat out

The Forward Assembly is now standalone