F18 Startup

Plug in Access Point
Connect all devices to power
Power on projectors using Mega RS232 control – check all have started
Power on the Simulator using the Power Switch located next to the throttle.
Monitor startup actions of gauges and back panel lighting
Power on Amplifier and set input to DVD
Wait until Projectors have completed their startup sequence
Power on PC
BIOS should be displayed on Center Projector
Logon to Windows
- If floor is squashed – shutdown and restart
- Check all monitors are displaying desktop
run CheckSim.cmd – ensure all devices are responding to pings
Start SOCAT cmd file and validate all COM ports count down to 0.
Start Fly Elise – disable Windows Warping if enabled
Start DCS
Start Flight
Enable Desktop Warping