Radio Code working document

ENCODER_PIN_A, ENCODER_PIN_B: These define the digital pins connected to your encoder. You can choose any available digital pins on the Arduino Due.
- volatile variables: encoderValue, lastEncoderChangeTime, and encoderDirection are declared volatile. This tells the compiler that these variables can be changed by something outside the normal program flow (i.e., by an interrupt), preventing optimizations that might lead to incorrect values.
- setup():
  - Serial.begin(115200): Initializes serial communication for debugging output.
  - pinMode(ENCODER_PIN_A, INPUT_PULLUP): Configures the encoder pins as inputs and enables the internal pull-up resistors. This is important for stable readings.
  - attachInterrupt(digitalPinToInterrupt(PIN), ISR_FUNCTION, CHANGE): This function sets up the external interrupts.
    - digitalPinToInterrupt(): Converts the digital pin number to the specific interrupt number for the microcontroller.
    - readEncoder: This is the Interrupt Service Routine (ISR) that will be called when an interrupt occurs.
    - CHANGE: The interrupt will trigger whenever the pin's state changes (from HIGH to LOW or LOW to HIGH). Attaching to both pins with CHANGE mode is a robust way to capture all encoder events.
- readEncoder() ISR:
  - Debouncing: DEBOUNCE_DELAY_US is used to ignore very rapid changes that are likely electrical noise or switch bounce, ensuring more accurate readings.
  - Quadrature Decoding: The if (pinA_state == pinB_state) logic is a common and fast way to determine the direction of rotation for a quadrature encoder when using CHANGE interrupts on both pins. You might need to swap 1 and -1 if your encoder's wiring results in the opposite direction.
  - Minimal Operations: The ISR only reads pins, performs a simple comparison, updates a direction flag, and records the time. The actual encoderValue update and acceleration logic are left to the loop() function.
- loop():
  - Critical Section: noInterrupts() and interrupts() are used to create a "critical section" when reading the volatile variables. This ensures that the ISR doesn't modify these variables in the middle of loop() reading them, preventing inconsistent data.
  - Acceleration Logic:
    - It calculates timeSinceLastChange since the last encoder step.
    - If timeSinceLastChange is less than FAST_TURN_THRESHOLD_US, it means the encoder is being turned quickly, so actualStep is multiplied by ACCELERATION_MULTIPLIER.
    - encoderValue is then updated with this (potentially accelerated) step.
  - Serial Output: The current encoder value, the step applied, and the time since the last change are printed to the Serial Monitor for observation.
Web references:
1. youtube.com
2. digikey.com
3. allaboutcircuits.com
4. blogspot.com
5. phippselectronics.com
6. embedded.com
7. runtimerec.com
8. arduino.cc
9. upesy.com
10. github.com
11. youtube.com
12. reddit.com
13. garrysblog.com

The Arduino Due's ability to have all digital pins support interrupts makes it highly suitable for projects requiring multiple rotary encoders. To add support for 5 additional encoders (making a total of 6), we'll extend the previous code by using arrays for encoder data and creating a dedicated Interrupt Service Routine (ISR) for each encoder.

### xplanation of Changes:
1. NUM_ENCODERS Constant: A new constant NUM_ENCODERS is defined to easily manage the number of encoders.
2. Pin Arrays: ENCODER_PINS_A and ENCODER_PINS_B are now arrays, holding the digital pin numbers for each encoder. I've chosen consecutive pins (2,3; 4,5; etc.), but you can use any available digital pins on the Due.
3. Volatile Variable Arrays: encoderValues, lastEncoderChangeTimes, and encoderDirections are now arrays, with each element corresponding to one encoder. This allows for independent tracking of each encoder's state.
4. Dedicated ISRs:
  1. Since attachInterrupt() requires a function pointer without arguments, each encoder needs its own ISR function (e.g., readEncoder0, readEncoder1, etc.).
  2. Each of these ISRs is responsible for handling the events for its specific encoder. Inside readEncoderX(), it accesses the corresponding elements in the encoderValues, lastEncoderChangeTimes, and encoderDirections arrays using its fixed index ([0], [1], etc.).
  3. An encoderISRs array of function pointers is used in setup() to simplify attaching interrupts in a loop.
5. setup() Loop: The setup() function now uses a for loop to:
  1. Configure the INPUT_PULLUP mode for both pins of every encoder.
  2. Attach the dedicated ISR to both the A and B pins of each encoder. This means that a change on either pin of a given encoder will trigger its specific readEncoderX() function.
6. loop() Loop: The loop() function also uses a for loop to iterate through all NUM_ENCODERS, processing their state, applying acceleration, and printing output. The critical section (noInterrupts() / interrupts()) is applied for each encoder's data access to ensure data integrity.
This setup efficiently handles multiple encoders with individual acceleration logic, leveraging the Arduino Due's extensive interrupt capabilities.

Serial Printing without blocking

To send data out the second serial port (Serial1) on an Arduino Due using interrupts in a non-blocking manner, you need to implement a transmit buffer (often a circular buffer) and leverage the UART's transmit-ready interrupt. This allows your main program (loop()) to continue executing without waiting for each byte to be sent.
The Arduino Due uses the SAM3X8E microcontroller, which has dedicated hardware for its serial peripherals (USARTs). Serial1 on the Arduino Due corresponds to USART1 on the SAM3X8E.

On the Arduino Due, Serial2 corresponds to USART2 on the SAM3X8E microcontroller. Its default pins are usually TX2 on digital pin 16 and RX2 on digital pin 17.

#include <Arduino.h>

// --- Configuration ---
#define TX_BUFFER_SIZE 256 // Size of the circular transmit buffer for Serial2

// --- Circular Buffer Variables ---
// These variables are shared between the main loop and the ISR,
// so they must be declared 'volatile'.
volatile char txBuffer[TX_BUFFER_SIZE];
volatile uint16_t txHead = 0; // Index of the next byte to be written into the buffer by the main loop
volatile uint16_t txTail = 0; // Index of the next byte to be sent from the buffer by the ISR
volatile uint16_t txCount = 0; // Number of bytes currently in the buffer

// --- Function Prototypes ---
void setupSerial2NonBlocking();
bool serial2WriteNonBlocking(const char* data, size_t len);
bool serial2PrintNonBlocking(const char* str);
bool serial2PrintlnNonBlocking(const char* str);

// --- ISR for Serial2 (USART2) Transmit ---
// This ISR is called when the USART2 Transmit Holding Register (THR) is empty
// and ready to accept new data.
void USART2_Handler() {
  // Check if the transmit ready interrupt flag is set and enabled.
  // US_CSR_TXRDY indicates the Transmit Holding Register is empty.
  // US_IMR is the Interrupt Mask Register, checking if TXRDY interrupt is enabled.
  if ((USART2->US_SR & US_CSR_TXRDY) && (USART2->US_IMR & US_CSR_TXRDY)) {
    if (txCount > 0) {
      // There is data in our circular buffer to send
      USART2->US_THR = txBuffer[txTail]; // Write byte to Transmit Holding Register
      txTail = (txTail + 1) % TX_BUFFER_SIZE; // Move tail pointer
      txCount--; // Decrement count of bytes in buffer
    } else {
      // No more data in the buffer, disable the TXRDY interrupt
      // to prevent continuous triggering until new data is added.
      USART2->US_IDR = US_CSR_TXRDY;
    }
  }
}

// --- Setup Function ---
void setup() {
  // Initialize the primary Serial port for debugging output to the programming port
  Serial.begin(115200);
  while (!Serial && millis() < 5000); // Wait for Serial port to connect (optional, for some boards)
  Serial.println("Arduino Due Non-Blocking Serial2 Transmit Example");

  setupSerial2NonBlocking(); // Initialize Serial2 for non-blocking transmit
  Serial.println("Serial2 configured for non-blocking transmit on pins 16 (TX) and 17 (RX).");
}

// --- Loop Function ---
void loop() {
  static unsigned long lastSendTime = 0;
  const unsigned long sendInterval = 1000; // Send a message every 1 second

  if (millis() - lastSendTime >= sendInterval) {
    lastSendTime = millis();

    static int counter = 0;
    char msg[50];
    // Create a message to send
    sprintf(msg, "Hello from Due via Serial2! Counter: %d", counter++);

    // Attempt to send the message non-blocking via Serial2
    if (serial2PrintlnNonBlocking(msg)) {
      Serial.print("Queued for Serial2: ");
      Serial.println(msg);
    } else {
      Serial.println("Serial2 TX buffer full. Message dropped.");
    }
  }

  // Your main loop can do other things here without being blocked by Serial2 transmission.
  // For example, reading sensors, updating displays, performing calculations, etc.
  // This delay is just to prevent flooding the main Serial monitor for this example.
  delay(10);
}

// --- Non-Blocking Serial2 Initialization ---
void setupSerial2NonBlocking() {
  // Initialize Serial2 at 9600 baud (or your desired baud rate).
  // This function from the Arduino core handles pin setup, baud rate, etc.
  Serial2.begin(9600);

  // Configure NVIC (Nested Vectored Interrupt Controller) for USART2_Handler
  // Set priority (lower number = higher priority). Priority 1 is common.
  NVIC_SetPriority(USART2_IRQn, 1);
  // Enable the interrupt in the NVIC.
  NVIC_EnableIRQ(USART2_IRQn);

  // Initially disable the TXRDY interrupt. It will be enabled when data is
  // added to the circular buffer by serial2WriteNonBlocking().
  USART2->US_IDR = US_CSR_TXRDY;
}

// --- Non-Blocking Write Function ---
// Writes a block of data to the circular buffer.
// Returns true if all data was queued, false if the buffer became full.
bool serial2WriteNonBlocking(const char* data, size_t len) {
  bool wasEmpty;
  // Protect circular buffer access from concurrent modification by ISR
  noInterrupts();
  wasEmpty = (txCount == 0); // Check if buffer was empty before adding data
  interrupts();

  for (size_t i = 0; i < len; i++) {
    noInterrupts(); // Protect circular buffer access for each byte
    if (txCount < TX_BUFFER_SIZE) {
      txBuffer[txHead] = data[i];
      txHead = (txHead + 1) % TX_BUFFER_SIZE;
      txCount++;
      interrupts();
    } else {
      // Buffer is full, cannot queue this byte or subsequent bytes
      interrupts();
      return false; // Indicate that not all data was queued
    }
  }

  // If the buffer was empty before adding data, and now has data,
  // enable the TXRDY interrupt to start the transmission process.
  if (wasEmpty && txCount > 0) {
    USART2->US_IER = US_CSR_TXRDY; // Enable TXRDY interrupt
  }
  return true; // All data successfully queued
}

// --- Non-Blocking Print String Function ---
// Convenience function to print a null-terminated string.
bool serial2PrintNonBlocking(const char* str) {
  return serial2WriteNonBlocking(str, strlen(str));
}

// --- Non-Blocking Println String Function ---
// Convenience function to print a null-terminated string followed by CR+LF.
bool serial2PrintlnNonBlocking(const char* str) {
  bool success = serial2WriteNonBlocking(str, strlen(str));
  if (success) {
    success = serial2WriteNonBlocking("\r\n", 2); // Add Carriage Return and Line Feed
  }
  return success;
}

1. Circular Buffer:
  1. txBuffer, txHead, txTail, and txCount form a circular buffer. This buffer temporarily stores bytes that are waiting to be sent over Serial1.
  2. volatile keyword is essential for these variables, as they are modified by both the loop() function and the Interrupt Service Routine (ISR).
2. setupSerial1NonBlocking():
  1. Serial1.begin(9600); initializes the USART1 hardware peripheral (which Serial1 uses) for communication at 9600 baud. This sets up the necessary pins (TX1 on pin 18, RX1 on pin 19) and basic UART parameters.
  2. NVIC_SetPriority(USART1_IRQn, 1); and NVIC_EnableIRQ(USART1_IRQn); configure the Nested Vectored Interrupt Controller (NVIC) to enable interrupts for USART1 and set its priority.
  3. USART1->US_IDR = US_CSR_TXRDY; initially disables the Transmit Ready (TXRDY) interrupt. This interrupt will only be enabled when there's data in our txBuffer to prevent it from continuously firing when idle.
3. USART1_Handler() (The Interrupt Service Routine):
  1. This function is automatically called by the SAM3X8E microcontroller whenever an interrupt from USART1 occurs.
  2. It checks if the interrupt was specifically caused by the TXRDY flag (meaning the hardware transmit register is empty and ready for the next byte) and if this interrupt source is currently enabled.
  3. If txCount > 0, it means there's data in our txBuffer. The ISR takes the next byte from txBuffer (at txTail), writes it directly to the USART1->US_THR (Transmit Holding Register) hardware register, and updates txTail and txCount.
  4. If txCount becomes 0 after sending a byte, the txBuffer is now empty. The ISR then disables the TXRDY interrupt (USART1->US_IDR = US_CSR_TXRDY;) to stop further interrupts until new data is added.
4. serial1WriteNonBlocking(const char* data, size_t len):
  1. This is the core function for queuing data. It takes a pointer to the data and its length.
  2. It first checks if the txBuffer was empty before adding any new data. This check is crucial because if it was empty, we'll need to explicitly enable the TXRDY interrupt later to kick-start the transmission process.
  3. It then iterates through the provided data, adding each byte to the txBuffer and updating txHead and txCount.
  4. Critical Sections: noInterrupts() and interrupts() are used around modifications to txHead, txTail, and txCount. This prevents "race conditions" where the ISR might try to read or modify these variables at the exact same time the serial1WriteNonBlocking function is, which could lead to corrupted data or incorrect buffer states.
  5. If the buffer becomes full (txCount < TX_BUFFER_SIZE fails), it stops adding data and returns false, indicating that not all data could be queued.
  6. Finally, if data was successfully added and the buffer was previously empty, it enables the TXRDY interrupt (USART1->US_IER = US_CSR_TXRDY;). This tells the hardware to start sending the first byte and trigger the ISR when it's ready for the next.
5. serial1PrintNonBlocking() and serial1PrintlnNonBlocking():
  1. These are convenience functions that wrap serial1WriteNonBlocking to make it easier to send C-style strings, similar to how Serial.print() and Serial.println() work. serial1PrintlnNonBlocking also adds a carriage return and line feed (\r\n).
### To Use This Code:
1. Upload to Arduino Due: Compile and upload this sketch to your Arduino Due.
2. Hardware Connections:
  1. Connect a device (e.g., another Arduino, a USB-to-serial adapter, or a computer's serial port) to the TX1 (pin 18) and RX1 (pin 19) pins of your Arduino Due.
  2. Ensure the Ground (GND) of your Arduino Due is also connected to the GND of the receiving device.
3. Serial Monitors:
  1. Open the Serial Monitor in the Arduino IDE for the programming port (the one you use to upload code). This will show you the debug messages from Serial.
  2. Open a separate serial terminal program (like PuTTY, CoolTerm, or a second instance of the Arduino IDE's Serial Monitor if your OS allows) and configure it to connect to the serial port corresponding to your receiving device, at 9600 baud.
4. Observe Output:
  1. You should see messages like "Queued for Serial1: Hello from Due! Counter: X" appearing on your Arduino IDE's Serial Monitor.
  2. Simultaneously, you will see "Hello from Due! Counter: X" messages appearing on your second serial terminal, sent via Serial1.
This setup demonstrates how your loop() function can continue to execute other tasks (like the delay(10); or any other logic you add) without being blocked, while the Serial1 data transmission happens efficiently in the background via interrupts.

### Key Changes for Serial2:
1. ISR Name: The Interrupt Service Routine is now named USART2_Handler() instead of USART1_Handler().
2. Hardware Register Access: All references to USART1-> have been changed to USART2-> (e.g., USART2->US_SR, USART2->US_THR, etc.).
3. NVIC Configuration: In setupSerial2NonBlocking(), the NVIC_SetPriority() and NVIC_EnableIRQ() calls now use USART2_IRQn (the interrupt request number for USART2).
4. Serial2.begin(): The initialization now uses Serial2.begin(baudRate);.
5. Function Names: The wrapper functions for writing data are now serial2WriteNonBlocking, serial2PrintNonBlocking, and serial2PrintlnNonBlocking.
6. Comments: Updated to reflect Serial2 and its associated pins (16-TX, 17-RX).
### How to Use This Code with Serial2:
1. Upload to Arduino Due: Compile and upload this sketch to your Arduino Due.
2. Hardware Connections:
  1. Connect a device (e.g., another Arduino, a USB-to-serial adapter, or a computer's serial port) to the TX2 (digital pin 16) and RX2 (digital pin 17) pins of your Arduino Due.
  2. Ensure the Ground (GND) of your Arduino Due is also connected to the GND of the receiving device.
3. Serial Monitors:
  1. Open the Serial Monitor in the Arduino IDE for the programming port (the one you use to upload code). This will show you the debug messages from Serial.
  2. Open a separate serial terminal program (like PuTTY, CoolTerm, or a second instance of the Arduino IDE's Serial Monitor if your OS allows) and configure it to connect to the serial port corresponding to your receiving device, at 9600 baud.
4. Observe Output:
  1. You should see messages like "Queued for Serial2: Hello from Due via Serial2! Counter: X" appearing on your Arduino IDE's Serial Monitor.
  2. Simultaneously, you will see "Hello from Due via Serial2! Counter: X" messages appearing on your second serial terminal, sent via Serial2.
This setup provides a robust, non-blocking way to send data out Serial2, allowing your main program to remain responsive to other tasks.