The Jet Ranger Build

# 2025 Rebuild Notes

Now using MSFS2024 with Air Manager v5 to display 2d panels.

With the FlyInside 206 whilst chunks of the default 206 instruments work on the Air Manager 206 panel, the following gauges are not displaying correctly
- Engine Rotor RPM
- Engine Torque

Testing Cowan Sim 206

Installing COWAN Simulator

To install the CowanSim 206 for Microsoft Flight Simulator, first, ensure you can see hidden files on your computer by selecting "Hidden items" in the File Explorer's "View" tab. Then, extract the downloaded aircraft files and move them directly into the "Community" folder of your MSFS 2020 installation.

C:\Users\bnepe\AppData\Local\Packages\Microsoft.Limitless_8wekyb3d8bbwe\LocalCache\Packages\Community

Cowan Sim panewls not displaying correctly
- VSI
- Torque measures too higher-level
  - 72 →32
  - 90 → 42
  - 100 → 44
- No Transmission Oil Temperature and Pressure
- No Turbine Out Temperature

Gauges that are ok
- Eng Oil
- Fuel
- Load
- Gas Producer
- Airspeed
- Rotor and Turbine
- Radar Altimeter
- Attitude Indicators
- Altimeter
- Slip

msfs_variable_subscribe("ELECTRICAL MAIN BUS VOLTAGE", "Volts",
"CIRCUIT PITOT HEAT ON", "Pitot", -- Pitot
"FUEL TOTAL QUANTITY", "Gallons", -- Fuel < 17?
"FUELSYSTEM ENGINE PRESSURE:1", "PSI", -- Fuel pressure
"ROTOR CHIP DETECTED:1", "Bool", -- Main chip
"ROTOR CHIP DETECTED:2", "Bool", -- Tail chip
"A:ENG OIL PRESSURE:1", "PSI", -- XMSN press < 15?
"ENG OIL TEMPERATURE:1", "Celsius", -- XMSN temp > 115?
"ELECTRICAL BATTERY LOAD:1", "Amperes", -- Battery temp > 87 -- Battery hot > 130
"ENG N1 RPM:1", "Percent", -- N1 < 55
"ENG COMBUSTION:1", "Bool", -- False
"GENERAL ENG MASTER ALTERNATOR:1", "Bool", -- False
"FUELSYSTEM PUMP ACTIVE:1", "Bool", -- Fuel pump
"FUELSYSTEM PUMP ACTIVE:2", "Bool", -- Fuel pump
"ROTOR RPM PCT:1", "Percent", -- <= 95
"L:buttonAnnTest", "Double", new_warnings_fs)

function new_warnings_fs(volts, pitot, fuelq, fuelp, xmsn_chip, tr_chip, xmsn_press, xmsn_temp, bat_load, n1, combustion, alternator, pump_1, pump_2, rotor_rpm, test)

 power = volts > 10
    -- No function
    visible(img_mask[1], false)
    -- No function
    visible(img_mask[2], false)
    -- Pitot heat
    visible(img_mask[3], pitot and power)
    -- Fuel low
    visible(img_mask[4], fuelq <= 17 and power)
    -- AF fuel filter
    visible(img_mask[5], fuelp == 0 and power)
    -- Fuel filter
    visible(img_mask[6], false)
    -- Engine chip
    visible(img_mask[7], false)
    -- Battery hot
    visible(img_mask[8], bat_load >= 130 and power)
    -- Trans oil press
    visible(img_mask[9], xmsn_press <= 15 and power)
    -- Engine out
    visible(img_mask[10], (n1 <= 55 or not combustion) and power)
    -- No function
    visible(img_mask[11], false)
    -- No function
    visible(img_mask[12], false)
    -- No function
    visible(img_mask[13], false)
    -- No function
    visible(img_mask[14], false)
    -- No function
    visible(img_mask[15], false)
    -- Gen fail
    visible(img_mask[16], not alternator and power)
    -- Fuel pump
    visible(img_mask[17], (not pump_1 or not pump_2) and power)
    -- T/R chip
    visible(img_mask[18], tr_chip and power)
    -- Trans chip
    visible(img_mask[19], xmsn_chip and power)
    -- Battery temp
    visible(img_mask[20], bat_load >= 87 and bat_load < 130 and power)
    -- Trans oil temp
    visible(img_mask[21], xmsn_temp >= 115 and power)
    -- Low rotor RPM
    visible(img_mask[22], rotor_rpm <= 95 and power)
    -- Annunciator test
    visible(testfg, test == 1 and power)

end
# Todo’s

- Update Rotaries to stacked rotaries from Leo Bodnar
- Determine number of rotaries to set priorities
- ADF needs a 3rd rotary, in the mean time map the RH rotary, clockwise to increment 0.1’s, counter clockwise to increment 1s. LH rotary, clockwise to increment 10s, counter clockwise to increment 100s.
- Valid VOR tones are coming through headsets.
- Sent Grip to Jess
- Get to why Dodo isn’t playing with P3D 2.3
- Determine how to back up Linda configurations for Joysticks.
- Update table of output ports for SIOC USB Outputs card.
- Draw out audio system structure
- Remove fan interference when they are switched, either through the addition of ceramic caps, or using separate PSU for fans. This will mean modifying the overhead, panel so perhaps first test using plug pack PSU on a single fan, noise could be introduced through the common ground, so it may be easier to separate out the 5V supply and move it to the base. Other option is to use a 9V battery, would ideally use a rechargeable.
- Used a separate 5V supply and noise disappeared.
- Remove hum from overhead speakers, suggest grounding both (Left and right) inputs to amp to ground. Should be able to do this as rotary switch has 4 poles.
- Look at using DLL to get Dodo values to drive leads, code fragment is included dodo hardware interface document.

# The Build Process

FSX installed
Dodo, ran up no gauges displayed
Installed FSX Acceleration, Dodo gauges now displaying correctly
Installed DoDo SP2
Reasked about trusting the Dodo plugin
Installed FSUIPV
Pasted panel.cfg into the low skid
Panel undocked
On the Russ Cool Panel, the difficulty setting knob is located underneath the Temperate Display.

# CKAS Platform

As September 2025 two drivers are needed to interface the CKAS v4 6dof to MSFS2024. The drivers are bundled in GENERIC.ZIP found at:
 https://www.dropbox.com/scl/fo/8yi65aqoaf3mk41u2tdv7/ABmutMLNO-6xkF-Fy05Db7w?rlkey=fx4w5f69yghwtz3izafktot4d&dl=0

 Install SimCor (Setup CKAS SimCor.exe) and then SimDX (SimCorDX_207_Setup.exe).

Once installed rename simConnectShim.dll to not_used_simConnectShim.dll, this is needed to be done otherwise SimCor exits when MSFS2024 starts.

The COIMport of the platform should be set to COM19.

To start the platform:
- Apply power to the Platform
- Apply power and turn on the external 12V PSU. This is needed to arm the safety interlocks.
- Start SimCor – if the platform is correctly armed (including the safety switch inside the cabin), the platform will rise to a mid position. If the external 12V PSU is powered off the platform will return a the low park position.
- If so desired platform movement can be tested using the jog function. Note the vertical action appears inversed, i.e. if Z is dragged to the lower position, the platform rises. If you have tested the jog function – remember to return the input back to model

- Start SimCor DX, you may get a warning re the platform not responding if you have not returned the input on SimCor from Jog to Model , check the lower panels for status.

## CKAS Failure mode

In very rare occasions the platform has had a motor move out of step – in Sept Motor 4 moved to incorrect position. Cycling the power for the platform may help, but ultimately identified the positioning sensing belt must have slipped as the indexing marks were no longer aligned. Held the belt against the pot and adjust the belt and potentiometer to align. As part of troubleshooting noted the led at the top of the 4th motor controller was flashing red which suggests some form of over current protection was being applied. The motor controller leds all started green, and then once motors tried to move the motor controller led changed from green to red.

Please make sure to read how to do this correctly in the Legacy Mode section of the SimCorDX manual – you must ALWAYS run SimCor first! Then run SimCorDX afterwards.

Initially had an older CKAS driver, which exploded when running P3D.
The Drivers can be found at www.ckas.com.au/downloads/Setup%20CKAS%20SimCor.exe
As of Oct 2014 the file version is 1.0.0.21

# Building the Computer

### Install Operating System
- Turn on visibility of hidden files and file extensions in explorer
- If using Samsung SSDs optionally install the Samsung Drive Monitoring Software
  - http://samsung.com/magician
#### Assign Static IP Address to Ethernet Connecting to Pit

Control Panel → Network and Internet → Network Connections. As the simple interface demands a default gateway and DNS be set, which is not used for this interface.
A static address (172.16.1.10/24) is used to receive switch events for MSFS 20202 as well as monitoring updates from the Arduino environment. If this address is not defined DCS interfaces will operate but updates may be slow due to the Arduino waiting for a timeout in resolving the ARP for the reflector. If it is not planned to use this link then is it recommended the following values be set to 0 in the Arduino code.
#define Reflector_In_Use 1
#define MSFS_In_Use 1
### Install Documentation Tools
These tools were chosen as they are cross-platform and lightweight
- LibreOffice - https://www.libreoffice.org/
- Draw.io – Offline installer – https://get.diagrams.net/.
  - Primary site - https://www.diagrams.net/
### Install Development Environment
- Install Github –
  - http://desktop.github.com/
  - add primary repository -
    - https://github.com/bnepethomas/bne-arduino-flight-simulator-interfaces
- Instal Notepad++ https://notepad-plus-plus.org/downloads/
- Install Arduino IDE – including libraries used (built-in if author is not listed)
  - https://www.arduino.cc/en/software
  - Ethernet – 2.0.2
  - Keyboard – 1.0.6
  - Mouse – 1.0.1
  - Servo 1.2,2 – Michael Margolis
  - Stepper 1.1.3
  - AccelStepper – 1.64.0 – Mike McCauley
  - Adafruit GFX Library – 1.12.2
  - Adafruit SSD1306 – 2.5.15
  - LedControl – 1.0.6 – Eberhard Fahle
  - U8g2 – 2.35.2 – oliver
  - U8g2_for_Adafruit_GFX – 1.8.0 – oliver
  - DCS-BIOS 0.3.1 - Puma
- Install Python – minimum release 3.10 (for Case Statement support)
  - Add python.exe to PATH
  - Install python modules
    - pythonping (used in pyHWLink_System_Check.py)
    - SimConnect. Originally I had to use a fork on SimConnect, but the original project https://github.com/odwdinc/Python-SimConnect has now fixed the error, so using it.
      - Pip install SimConnect (0.4.26)
      - The module will be validated once MSFS 2000 has been installed.

### Install Utilities

- Nirsoft Multi Monitor Tool
  - https://www.nirsoft.net/utils/multi_monitor_tool.html
- Nirsoft Device Viewer
  - https://www.nirsoft.net/utils/device_manager_view.html
- USB Tree View
  - https://www.uwe-sieber.de/usbtreeview_e.html#download
  - To test restart USB by command line
  - https://www.uwe-sieber.de/misc_tools_e.html#restartusbport
- Wireshark
  - https://www.wireshark.org/download.html
- Auto Logon from Sys Internals
  - https://learn.microsoft.com/en-us/sysinternals/downloads/autologon
  - Run autologon so login occurs automatically – may want to create a local account.

### Install Backup/Imaging Software
Currently use Acronis True Image – but the perpetual licenses are no longer available – so may need to look for alternatives.
### Install DCS
### Install MSFS 2020
- Start MSFS 2020 and sign in
- Run ‘Python HW Link\pyHWLink_SimConnect_Transmitter.py’
### Install Fly Elise
- Play the USB dongle in a port
- Install Fly Elise Display Pro (https://fly.elise-ng.net/immersive-display-pro/) Version 4.5.3
- Start Fly Elise Display Pro and Validate correct details are displayed in the license screen
- Install Fly Elise Calibration Pro Version 5.0.2. Download Zip, extract and then copy to a folder.
- Refer to “Building and Deploying A Curved Screen” for further details. Of note is the importance of allocating keystrokes to:
  - Start Warp
  - Stop Warp
  - Enable 2D Warping
  - Enable 3D Warping
- Start MSFS 2020 and validate screen is correctly displayed. MSFS SU10 enabled Surround and multiscreen support which improves the curved screen experience. Largely it reduces the distortion encountered ad the edges of the screen, ideally meaning lampposts are no longer leaning over. The Fly Elise team have noted that the surround view support still has room for improvement (as of Oct 2022).
### Install Orbx Central
- Note different pits may operate under different accounts
- Download scenery of interest
### Configure DCS
Start DCS and load desired modules (eg Syria, Hornet)
### Install and Configure Flight Panels DCS-BIOS

- Clone in GitHub Desktop https://github.com/DCS-Skunkworks/dcs-bios
- Should have already install Arduino DCS-BIOS library.
- Connect the pits USB port
- Statically assign COM Port numbers for the Arduino’s using the noting the Arduino Serial Numbers
- Ben’s document provides a useful guide to setting up Flight Panels DCS-BIOS fork (DCS-BIOS-FLIGHTPANELS.pdf)
  - THE FOLLOWING STEPS NEED TO BE VALIDATED!
  - Extract and copy the SOCAT.EXE to the programs directory within the git Repo
  - Edit the batch file to reflect the serial ports in use.
  - Add a taskbar shortcut to the CMD file – Error: Reference source not found
# Output Card

Open Cockpits (OC) hardware is both cost effective, and once you’ve got your head around it, very flexible, the biggest challenge is getting started.

To test the USB output card use test_outputs.exe, this is a simple to use GUI for turning outputs on/off. It can also be used to see what are the device numbers associated with each card. Note these device numbers are likely to change if you inserted them into a different USB port. If you are unsure which is which ground one of the analog inputs, the other inputs will jump around.

For testing LHS is 169, RHS is 114.

The modules generally communicate to the hardware via a SOIC Server that uses compiled scripts to map incoming variables from the simulator to OC hardware. The output module needs to be linked to script variables.
1. Start SOIC Server
2. If the OC card is not already plugged in, plug it in
3. You should see an entry in the devices box in the top right hand corner
4. Click the config devices button
5. If the device is not already configured you’ll see the card’s ‘Script Device IDX’ is not defined, and the Master Status is ‘not linked’ in the right hand window. To link, click the USBOutputs line on the left hand box, and the Master entry in the right hand box, then the link button.
6. Save and Exit.

For testing Mapped 169 as Master (IDX=0) and 114 as IDX = 1

If you are using multiple USB Output cards, one will be the Master, the second will be unlink. Click on the card whose IDX is ‘Not Defined’ and enter a script IDX in the center text box. Click ok and save.

For testing – normally do not specify Device Number (Dispositivo?), assigned Device Number 1 to T/O Trim 191. Done by click Edit Script, Double Clicking on Var and assigning value. File Save, Close Window, click Reload.

Now go into IOCP Console, Connect, Log On. Set value of Var 191 to 1. Test switch holds position.

For final test, added another card, Device 164 in USB Outputs. Changed Device IDs, 169=0, 164=1, 114=2.

Dimming USB Outputs

As two of the three USB Output cards are driving leds, they should be dimmable. The card driving Magnetic switches and relays should be a fixed output.

Here’s the sample script:
Var 0002, name dimmer, Link IOCARD_ANALOGIC, De
vice 1, Input 1, PosL 1, PosC 128, PosR 255
// potentiometer reading
{
&bright = &dimmer
}
Var 0003, name bright, Link IOCARD_DISPLAY, Device 1, Digit 1, Numbers 3 // dimmer at USB Outputs

The steps to create the script:
Go into Script Editor and create all the variables (basically assigning a name to an output or handle).
Once this is done click on the input value that will be used to set the outputs, and choose edit-> New Command. From there you create an assign of source var to destination variable. In the GUI the commands should appear under the input variable. Note – you need to ensure you have selected the input variable when adding the commands

Var 0003, Link IOCARD_OUT, Device 1, Output 0
Var 0004, name dimmer, Link IOCARD_ANALOGIC, Device 2, Input 0, PosL 1, PosC 128, PosR 255
{
  &bright = &dimmer
  &bright2 = &dimmer
}
Var 0005, name bright, Link IOCARD_DISPLAY, Digit 1, Numbers 3
Var 0006, name bright2, Link IOCARD_DISPLAY, Device 1, Digit 1, Numbers 3

The Output Cards variables are mapped in the primary .ssi associated with the SOIC server.
# IP Port Utilisation

Application	Client/Server	TCP/UDP	Port	Partner Applications

SOIC Server	Server	TCP	8092	IO Card LCD,
IO Card LCD	Client	TCP	8092	SOIC Server
SOIC_Conv	Client	TCP	8092	SOIC Server
SOIC_Conv	Server	UDP	7777	DCS World – Receives comma delimited data from DCS
SOIC_Conv	Server?	UDP	7779	DCS World?
SOIC_Conv	Client	UDP	7780	DCS World / CDU Keystrokes send to DCS
DCS World	Server	UDP	7780	SOIC_Conv – Receives CDU Keystrokes from SOIC_Conv
Arduino Display	Server	UDP	7781
GPS Out	Server	UDP	7782	Receives UDP packets from BeforeNextFrame and reformats to serial with checksum for GPS
Simmeters	Server	UDP	6061	DCS World – Receives comma delimited data from DCS

# GPS Out

Use native interface in FSUIPC. Note after you have added the GPS configuration in FSUIPC, it does not send anything out to the GPS until you restart FSX. It also identified that COM7 for the Arduino was in use, so didn’t offer it up as a choice.

# GPS Setup

The GPS takes a serial NEMA data feed.
System Setup
Communications Port
Baud Rate 19200
NEMA Input
NEMA GPS Input
Configure NEMA
GLL, RMC and RMB, GGA, GSA and GSV, APB

Software version 1.7.0

Cable Pinout

DB9
DB9			Lowrance
1	Gnd	Black	3
2
3	RX RS-232	Green	2
N/C		White	N/C
N/C	+12V	Red	1

Pin connector as seen from back of Airmap 2000C

Pin	Name	Description
1	VCC	Power
2	RX	RS-232 (receive serial)
3	GND	Ground
4	TX	NMEA/Pseudo RS-232 (transmit serial)
5	-	DO NOT USE (recharging purposes)
6	-	DO NOT USE (recharging purposes)

Was unable to buy an original NEMA cable, so had to modify a power only cable.
Modifying a power cable to a NEMA cable
1. Purchased a DB25 headshell with pins to be placed.
2. Drill out pin 2 of existing existing power connector with a 1mm drill all of the way through to the back for the cable.
3. Drill out pin 2 with a 3mm drill only partially so that the pin is able to seat in the socket without being able to be pushed all the way through
4. Heat Glue DB25 socket connector in Lowrance connector.

# Driving the OLEDs

The OLEDs use an I2C bus, which enables all of the OLED displays to be connected to a single Arduino card. The only challenge encountered when using this approach is that a ‘demultiplexor’ (demux) is needed as all of the OLED displays have the same I2C bus address.

In addition to enabling the OLED displays to be uniquely addressed in S/W. the demux buffers the output which reduces the likelihood of issues associated with longer cable runs. Uniqueness is achieved by ANDing SCL with one of the Digital outputs. Initially SDA was also going to be buffered, but for reasons I’m yet to work out, the displays did not appear to receive data when SDA was buffered, if may be due to clock-skew and issues associated with not having pull-up resistors. As the system is currently working, I’m reluctant to attempt to fix it. The displays are never read, only ever written to.

Another benefit of using common OLEDs is initialisation codes can be ‘broadcast’ to all attached displays, this is done by raising all of the Data Outputs to high. This is used to initialise all of the attached displays.

Generally ‘clearing’ displays is avoided as this incurs a performance hit. Displays are updated an entire line at a time, with trailing spaces to pad out the display.

As the Arduino is presented via a USB-Serial interface there is a ‘serialisation tax’ which must be taken into consideration when sending data to the Arduino card. The performance tax is minimised by setting the UART to run at 115,200bps. As a very simple protocol is used to send data to the displays, the rate at which updates are send must not cause ‘tail drop’ in the UART, this will result in corrupted data being displayed. A 50mS delay appears to be adequate during most updates. A good test of timing is to do a chaff/flare dump.

 Protocol between Arduino-multi-oled-receiver and Arduino card:
## Initialisation Sequence

Write out 2 * Nulls - _serialPort.Write(NULL, 0, 1);
Clear each display - ClearArduinoDisplay(oled1)
Send information text to each display - SendToArduino(oled1, FirstLine, "1 Waiting for DCS");

## Transmit Data to oled

SendToArduino(oled6, FirstLine, lastVHF_FM.PadRight(16));

Parameter / No
1	Oled Number – oled 1 to oled 6
2	Line Number – either FirstLine or Second Line
3	Text to be displayed – ASCII text – should be padded to end of display

There are two routines that actually send data to the Arduino

static void SendToArduino(byte[] oledPtr, byte[] lineNumber, string StrToSend)
{
if (_serialPort.IsOpen)
       {
_serialPort.Write(STX, 0, 1);
_serialPort.Write(oledPtr, 0, 1);
_serialPort.Write(lineNumber, 0, 1);
_serialPort.Write(StrToSend);
_serialPort.Write(ETX, 0, 1);
}
}

static void ClearArduinoDisplay(byte[] oledPtr)
{
if (_serialPort.IsOpen)
{
_serialPort.Write(STX, 0, 1);
_serialPort.Write(oledPtr, 0, 1);
_serialPort.Write(FirstLine, 0, 1);
_serialPort.Write(CLS,0,1);
_serialPort.Write(ETX, 0, 1);
}
}

This is called from branches which do a comparison against the last line sent to a given line on a given display.

There are two sources of data for the OLED displays, the first is data directory from DCS via LUA script, the second is from the ‘memory extractor’, cryptically called ‘bne-ocr-oled’, as this initially used Overpro’s OCR code, but now uses Gravils? Memory extractor. Both of these deliver the data over UDP using a variable name = value string. The data from the memory extractor is identified with a ‘9999’

// CMSC/CMSP has a tag attrbitue of 9999
       if (Get_Value(words,9999) == " ")

The bne-ocr-oled generated the entire line to be displayed, whereas the data delivered using the native LUA interface needs to be formatted.

### Native LUA data

// VHF
sWorkstr = "VHF FM " + Get_Value(words, 143) + Get_Value(words, 144) + Get_Value(words, 145) + "." + Get_Value(words, 146);
if (sWorkstr != lastVHF_FM)
{

lastVHF_FM = sWorkstr;
       SendToArduino(oled6, FirstLine, lastVHF_FM.PadRight(16));
       Thread.Sleep(20);
}

### Preformatted data from bne-ocr-oled

if (returnData.IndexOf("CMSP") > 0 )
{

if (returnData != lastCMSP)
       {
        SendToArduino(oled7, FirstLine, returnData.Substring(12, 18));
        Thread.Sleep(50);
        SendToArduino(oled7, SecondLine, returnData.Substring(32));
        Thread.Sleep(50);
        lastCMSP = returnData;
    }

}

## The Arduino Sketch

Unlike a UDP packet, an asynchronous serial port does not intrinsically have a Start-Of-Message, End-Of-Message construct; this has to be defined using a higher-level protocol. The Arduino runs a Finite State Machine to keep track of state.

// FSM States
#define stateWaitingForSerialData 0
#define stateLookingForStartOfMsg 1
#define stateLookingForOLEDPtr 2
#define stateLookingForLinePtr 3
#define stateRxAndDisplayChar 4

#define minoledPtr 1
#define maxoledPtr 7

#define minLinePtr 1
#define maxLinePtr 2

// Map Output Pins to OLED Displays
int oled1 = 2; // First usable output pin is D2 so all pins are incremented by 2
int oled2 = 3;
int oled3 = 4;
int oled4 = 5;
int oled5 = 6;
int oled6 = 7;
int oled7 = 8;

After the hardware initialization strings have been broadcast to all attached OLEDs, the number of each OLED is displayed, this is primary for troubleshooting, there is a brief delay, and then waiting for DCS is send to al displays.
In addition to the OLEDs themselves, each of the AND gates selection legs has an LED which is illuminated whenever that gate is selected.

Arduino Sender

A simple interface that drives multiple OLED displays off a single Arduino. The formatting of strings is performed on the host PC, leaving the Arduino to act as a Serial to I2C bridge/mux. As the OLED displays have the same target I2C address on the I2C bus the system must either have a bunch of Arduino’s (which means more USB ports and space consumed in the pit), or a muxing mechanism is added to software select the display to send data.

Principles:
Keep the Arduino code real simple, basically it receives a 5 part message
1. SOM (Start of Message)
2. Display Ptr (which display is the text going to)
3. Line Ptr (the original displays had two lines, so select which line the text is destined for)
4. Text (including trailing spaces to overwrite all previous displayed text)
5. EOM

The I2C bus is unidirectional ,i.e. the displays are never queried, it is assumed the data was received.

Start-up

On start the Arduino initialises all OLED displays, raising all Output

Hardware:
1. Currently a 4081 Quad AND gate is used. For some reason the I2C Clock (A4 pin) cannot be buffered via a AND gate. So there may be issues with Bus loadings as displays are added. It also could be due to not having a pull up resistor on the input to the gate
2. The initial design had the LEDs tied to the +5V rail, this means they are lit when the output is low.
3. Output pins D0 and D1 are used for internal purposes, so the first pin used is D2.

Variable	O/C Variable	OC OutputPort[1]
Com1 Transmitt	100	48
Com2 Transmitt	101	50
COM RxBoth	102	49
Nav1 Sound	103	44
Nav2 Sound	104	43
Marker Sound	105	42
DME Sound	106	41
ADF1 Sound	107	40
Inner Marker	110	45
Middle Marker	111	46
Outer Marker	112	47
Eng Out	120	23
Rotor Low	121	24
Fuel Low	122	33
Generator Fail	123	38
Battery Warm	124	31
Battery Hot	125	32
Fuel Pump Fail	126	39
Transmission Pressure Fail	127	25
Transmission Temperature Fail	128	26
Engine Chip	129	30
Tail Rotor Chip	130	21
Transmission Chip	131	29
Fuel Filter Fail	132	22
Baggage Door	133	20
SimConnect Fail	134	28
Spare1	135	37
Spare2	136	36
Spare3	137	35
Spare4	138	34
Spare5	139	27
AP_Master Switch	300
AP_Nav1 Lock	301
AP_Heading Lock	302
AP_Alt Lock	303
AP_IAS Lock	304
AP_Appr Lock	305
AP_BC Lock (Back Course)	306
AP_FD	307
[1] Starts at 0

# Overhead Panel

The Map reading light has it’s own switch, which is not mechanical, this means it cannot be controlled via an external toggle.

From back 1 is left

Power Distribution (need to add 12V permanent output for flexi light)

1:	12V Input
2:	GPS
3:	Cockpit Lights
4:	Not Connected
5:	5V Out to intercom

	Pins
HTR	7 – 11
Dir Gyro	29
Pitot Head	61
Avionics	45
Battery	60
Start-Gen	44
Heat-Vent - Heat	13
Heat-Vent – Vent	12
Gen Field	28
Gen Reset	59
Anti Coll	27
Pos Light	43
Fuel Boost Aft	26
Fuel Boost Fwd	42
Caution Light	58
Landing Light	25
Inst Light	41
Cockpit Light	Power Dist	Panel Backlighting
Strobe	57
Aud	Power Dist	Intercom
GPS	Power Dist
Co-Pilot Blower	Power Dist
Pilot Blower	Power Dist
Inst Light Dimmer	3 Pin to Power Dist

Inputs

Jaycar Keypad
3+2	1+2	5+2
1	2	3
3+7	1+7	5+7
4	5	6
3+6	1+6	5+6
7	8	9
3+4	1+4	5+4
*	0	#

## Configuring Switches

High Level Steps

Clear Axis for all joysticks
For Dodo need to specifically map throttle cutoff

Clear switch mapping for both toggles and rotaries
Suggest using first value at the top of the list when configuring. Click to remap action, if the switch is available/unused, then move to next switch, and then clear.

Use list of overhead switches to verify which ones can be mapped. One that may not have been done if the warning circuit breaker.

Preference would be to use the native interface in FSUIPC, as hopefully it is more timely than LINDA. There are limitations however, FSUIPC only recognises the first 32 buttons, so perhaps LINDA is more appropriate.

Suggested panel order
Radio Stack – not forgetting the Transfer/Switch button
ADF Panel

The DodoSim 206 FSX does not require FSUIPC to operate.  All the switch functions can be mapped using standard and non-standard key assignments as detailed within the manual.  However, most of these are toggle functions and therefore not ideal for use in hardware cockpits where specific On/Off or Fwd/Both/Off (as in landing lights) switch commands are needed.
Recent versions of FSUIPC4 for FSX offers a useful feature which the 206 (v1.054) makes use of, giving pit builders a whole host of new potential event bindings.  Here's how to use them:
1) Create a text file in notepad within the 'Flight Simulator X/Modules/' folder alongside the FSUIPC4.dll called 'DodoSim206FSX.evt' (The file folder is called Events
The entry inside the folder is  EventFiles)
2) Put the following text within the file:
Code Sample
[Events] 1=DODOSIM206FSX.ELECT_FUEL_PUMP1_SET 2=DODOSIM206FSX.ELECT_FUEL_PUMP2_SET 3=DODOSIM206FSX.WARNING_HORN_CB_SET 4=DODOSIM206FSX.NAV_LIGHTS_SET 5=DODOSIM206FSX.DIFFICULTY_LEVEL_SET 6=DODOSIM206FSX.DIFFICULTY_LEVEL_INC 7=DODOSIM206FSX.DIFFICULTY_LEVEL_DEC 8=DODOSIM206FSX.HEAT_VENT_SET 9=DODOSIM206FSX.GENERATOR_FIELD_CB_SET 10=DODOSIM206FSX.GENERATOR_RESET_CB_SET 11=DODOSIM206FSX.DIR_GYRO_SET 12=DODOSIM206FSX.MASTER_BATTERY_SET 13=DODOSIM206FSX.GENERATOR_SWITCH_SET 14=DODOSIM206FSX.ANNUNCIATOR_TEST_SET 15=DODOSIM206FSX.WARNING_MUTE_SET 16=DODOSIM206FSX.TURBINE_OVER_TEMP_TEST_SET 17=DODOSIM206FSX.GPS_DRIVES_NAV1_SET 18=DODOSIM206FSX.FUEL_VALVE_SET 19=DODOSIM206FSX.CAUTION_LIGHT_SWITCH_SET 20=DODOSIM206FSX.ANTI_ICE_SWITCH_SET 21=DODOSIM206FSX.HYDRAULICS_SWITCH_SET 22=DODOSIM206FSX.IDLE_RELEASE_SET 23=DODOSIM206FSX.TAXI_LIGHT_SWITCH_SET 24=DODOSIM206FSX.TAXI_LIGHT_SWITCH_OFF 25=DODOSIM206FSX.TAXI_LIGHT_SWITCH_ON

3) Open the FSUIPC.ini configuration file and look for a section called [Events].  If it isn't there, create one and enter the following data:
Code Sample
[EventFiles] 0=DodoSim206FSX

4) Restart FSX and open the FSUIPC dialog. Press a button to set an event assignment as normal, and look at the event selection list.  You'll notice a new set of bindings at the top, preceded by a : character, i.e.:
Code Sample
:DODOSIM206FSX.ELECT_FUEL_PUMP1_SET :DODOSIM206FSX.ELECT_FUEL_PUMP2_SET :DODOSIM206FSX.WARNING_HORN_CB_SET :DODOSIM206FSX.NAV_LIGHTS_SET ..etc..

5) When mapping a button to these functions, they require a parameter value.  As a rule, to set a switch off, use parameter 0, to set it on use 1.  Multi-position switches, such as the five position difficulty switch use parameters in the range 0-4, etc.

## P3D Installation

The up-shot is that if you copy the DodoSim 206 FSX over from an FSX installation to P3Dv2, it will work, but expect occasional crashes when re-loading aircraft or flights.  There is nothing that can be done about this.
To get the 206 FSX working to this state in P3D, you have to copy over from an FSX installation the following files:
1) The four DodoSim directories from within the /SimObjects/Rotorcraft directory.
2) The DodoSimFSX206.gau from the /gauges directory.
3) The fx_DodoSimEngineFire.fx file in the /effects directory.
Additionally, you will need some resources from the default FSX Bell 206 that the DodoSim 206 FSX uses:
1) Copy the whole /SimObjects/Rotorcraft/Bell206B directory over (to get the full set of external sounds)
2) Copy the /gauges/Bell_206B.dll file over (to get the default instruments used in places

POST REASSEMBLY CHECK ESTOP AND DOOR SENSOR
Overall removal order
Rudders
Seats
LH collective
Stop panel and removed door
Centre collective
Remove cyclic weight
Remove cyclic - clearance tight for console
Removing Seat Base
Remove Seats
Remove collective assembly as a whole
Cut cable ties holding cable assembly underneath
Remove SB external
Unplug SB rear speakers
unscrew SB volume control
Remove SB external USB cable from cable clamp
Place all cables in centre bay
Clear rear Cambridge speakers
Remove 4 coach screws holding frame
Centre pedestal installation
Install pedals first as they provide cantering info
Centre removal
GPS support
Radio Panels
Cover on front panels
  Screws base
  Bolts top
If removing front facia
  Bolt at bottom right
  Six bolts at top
Top maintenance
Slid left and right panels straight back and up to extract.  They catch on bolt at the front otherwise
Roof
  Install switch panel
  Starboard side- access with Port
  Slide port in from inside up back forward
  Position port with bolt
  Use mirror to locate screw hole
Side ceilings can be removed independently
GPS
Need to install USB to serial driver
4800 bps 500mS interval
FSUIPC
GGA, GSV, RMC, GLL, GSA.
Note GPS data is not sent if in FSUIPC menu.
Lowrance GLL, GGA, 4800 bps. NMEA Input, NMEA GPS INPUT.
Caused blue screen whel plugging in new GPS lead
On first boot with new USB hung at post.  Install driver for USB to serial PL-2303
Need to unplug and plug to recognise.
Intercom
Cigarette lighter has centre positive at 12 volts
If voltage presented is greater than 9 volts on passenger 3 and 4 output runs nicely down to 5 volts, so using 7805.
Main input not squelched out, recorder in is squelched.
DO NOT USE SOCKETS ON OVERHEAD PANEL - Headset cables will block video.
Drill out heads for attaching centre console to floor, needs to be below top face so electronics will fit.
LED backlighting
White
-|>-                  500 ohm 15.2mA
-|>- -|>-           330 ohm (330 a10) 15.5 mA
-|>- -|>- -|>-    150 ohm (220 a10)  13.2 mA
Led down lights
Removed all electronics
@17.2V 203.7mA
Cold 193-201mA as they warm up
So for 19v drop 2v @ 200mA is 10 ohms
W=V*A
=2 * 0.2
=0.4w around 0.5watts
@18v 1V @ 200mA = 5 ohms
W = 1 * 0.2
= 0.25 watts
Code based off
Bne-DCS-SOIC-cmd-line converter
Bne-arduino-multiled-receiver
For dodsim vars - run dodosim206fsxexportipc
Updates 0x2f28 - 8 byte concord nose visor
0  Engine out
1  Rotor Low
2  Fuel Low
3  Generator Fail
4  Battery Warm
5  Battery Hot
..
20. TOT
FSUIPC offsets
COM1	034E	2	BCD
COM1 Standby	311A	2	BCD
COM2	3118	2	BCD
COM2 Standby	311C	2	BCD
NAV1	0350	2	BCD
NAV1 Standby	311E	2	BCD
NAV2	0352	2	BCD
NAV2 Standby	3120	2	BCD

3122 Radio Audio 1 switches
2-7	Com1Tx
2-6	Com2Tx
2-5	Com RX Both
2-4	Nav 1 Sound
2-3	Nav 2 Sound
2-2	Marker
2-1	DMF
2-0	ADF

A leading '1' is assumed for all frequencies
SOIC
":" I between variables in UDP
Need to tie IO Card to script index
SOIC searches for script files from its directory, so if getting blank when editing or unable to find file while debugging, probably in wrong directory.
Debug can be used to set variables to light LEDs.
DO NOT FORGET TO RUN HARDWARE UTILITY TO GETTING WARNING PANEL STATUS FROM DODO.
----_nm ---_kt
DME     xxxx_nm  xxx_KT
XPonder xxxx
ADF xxx.x
Markers
O    Blue
M    Red
I      White
Radio
COM1  COM2  BOTH NAV1 NAV2 MKR DME ADF
Coding
Handle TCP disconnect - attempt to reconnect on next UDP packet.
Monitor avionics status on radio lights
Cleaned up Arduino code, removed special handling for LCD/OLED 2&7
Arduino (com4) -> arduino cli sender (UDP) -> fsx extractor (UDP) -> SOIC-conv (tcp) -> SOIC SERVER
Electronics
Found OverPros encoders not sending long enough pulses, so using Leo Bodnar encoders that supports encoders in a matrix.
Encoder is a ELMA E37 CT6330
Computer Build - SSD upgrade
Unplug unneeded USB devices, prevents hangs at reboot
Copied from 224G to 500G SSD took around 15min
Still need to increase partition size
Rebuild FSX installed, Dodo
Ran up, no gauges displayed
Installed FSX acceleration
Gauges displaying correctly
Installed Dodo SP2
Reasked about trusting
Installed FSUIPC
Pasted panel.cfg into low skid
Panel undocked
Difficulty setting knob underneath red text
On platform
Install FSUIPC in P3D 2.2
SimCor still crashed
Copied Dodo files as per Hover Controls instructions
Saved layout - 2nd Param in XML Is screen size
Deleted assignments for CHRC and BU0836X
Used new way of assigning toggles which works well.
Needed to use Toggle Tailwheel in FSX panel to get mute to work
Needed to set stop position in throttle within Dodo control panel
Also needed to map throttle to prop axis and tune in FSUIPC
On test computer downloaded build 3 of GoFlight SW
GF LEDs only on when avionics powered
Key send to other apps
LUA
FSx Linda enables the use of additional high count joystick controllers. FSX by default only recognises the first 32 inputs
To install copy to FSX modules folder
You are able to name stick
need to validate P3D compatibility
Config to start minimised when launched
Radio Audio Input Selector

COM1	66463
COM2	66464
Both	66465
Nav1	65842
Nav2	65843
Marker	66477
DME1	65844
ADF	65846

65637
65636
65644
65645
65638
65639
65646
65647
65642
65643
65640
65641
66437
66436
66438
66440

Switch/Rotary Mappings

Front Panel	Joystick
			F = FSUIPC starts 0 / L = Linda starts 1 / First Param Press, Second Param Release
Caution Light Test	None
Warning Horn Mute	1/23	F	Toggle Tailwheel Lock /0
TOT LT Test	1/22?	F	DODOSIM – Tot Test /1 /0
Altimeter Inc	1/7	F	Kohlsman Inc
Altimeter Dec	1/6	F	Kohlsman Dec
VOR1 Left Inc	1/0	F	VOR 1 Obi Inc Fast
VOR1 Left DEc	1/1	F	VOR 1 Obi Dec Fast
VOR1 Right Inc	1/8	F	Heading Bug Inc Fast
VOR1 Right Dec	1/9	F	Heading Bug Dec Fast
Nav/GPS	1/11	F	DODOSIM – GPS Drives NAV 1 /0 /1
Gyro Inc	1/4	F	Gyro Drift Inc
Gyro Dec	1/5	F	Gyro Drift Dec
VOR2 OBS Inc	1/2	F	VOR 2 Obi Fast Inc
VOR2 OBS Dec	1/3	F	VOR 2 Obi Fast Dec
Fuel Valve Open	1/10	F	DODOSIM – Fuel Valve Set /1
Fuel Valve Close	1/10	F	DODOSIM – Fuel Valve Set /1

Audio
COM 1	3/22	L	66463
COM 2	3/21	L	66464
BOTH	3/4	L	66465
Nav 1	3/38	L	65842
Nav 2	3/5	L	65843
MKR	3/7	L	66477
DME	3/20	L	65844
ADF	3/36	L	65846
COM 1 Swap	3/66	L	66372 – errs 3/97
COM 2 Swap	3/65	L	FSX: COM2 Radio Swap 0 errs 3/37
COM 1 Major Inc	4/1	L	65637
COM 1 Major Dec	4/2	L	65636
COM 1 Minor Inc	4/8	L	65639
COM 1 Minor Dec	4/7	L	65638
COM 2 Major Inc	4/19	L	66437
COM 2 Major Dec	4/20	L	66436
COM 2 Minor Inc	4/22	L	66440
COM 2 Minor Dec	4/21	L	66438
Nav 1 Swap	4/67	L	FSX NAV 1 Radio Swap err 4/51
Nav 2 Swap	4/52	L	FSX NAV 2 Radio Swap
Nav 1 Major Inc	4/16	L	65641
Nav 1 Major Dec	4/15	L	65640
Nav 1 Minor Inc	4/14	L	65643
Nav 1 Minor Dec	4/13	L	65642
Nav 2 Major Inc	4/4	L	65645
Nav 2 Major Dec	4/3	L	65644
Nav 2 Minor Inc	4/10	L	65647
Nav 2 Minor Dec	4/9	L	65646
AP HDG Inc	4/6	L	Unassigned
AP HDG Dec	4/5	L	Unassigned
AP V/S Inc	4/29	L	Unassigned
AP V/S Dec	4/30	L	Unassigned
AP CRS Inc	4/12	L	Unassigned
AP CRS Dec	4/11	L	Unassigned
AP Alt Inc	4/23	L	Unassigned
AP Alt Dec	4/24	L	Unassigned
AP IAS Inc	4/18	L	Unassigned
AP IAS Dec	4/17	L	Unassigned
AP CRS	3/3	L	Unassigned errs 3/16
AP HDG	3/17	L	Unassigned errs 3/33
AP IAS	3/18	L	Unassigned errs 3/34
AP ALT	3/19	L	Unassigned errs 3/35
AP APPR	3/49	L	Unassigned
AP Engage	3/18	L	Unassigned
AP FD	3/35	L	Unassigned errs 3/51
AP BC	3/50	L	Unassigned
Ident 1	2/79	L	FSX ATC Menu 1
Ident 2	2/78	L	FSX ATC Menu 2
Ident 3	2/80	L	FSX ATC Menu 3
Ident 4	2/127	L	FSX ATC Menu 4
Ident 5	2/126	L	FSX ATC Menu 5
Ident 6	2/128	L	FSX ATC Menu 6
Ident 7	2/111	L	FSX ATC Menu 7
Ident 8	2/110	L	FSX ATC Menu 8
Ident 9	2/112	L	FSX ATC Menu 9
Ident *	2/95	L	FSX Pause Toggle
Ident 0	2/94	L	FSX ATC Menu 0
Ident #	2/96	L	FSX ATC –Brings up ATC Window
ADF Major Inc	4/32	L	FSX ADF 100 Inc
ADF Major Dec	4/31	L	FSX ADF 100 Dec
ADF Minor Inc	4/26	L	FSX ADF 1 Inc (this is due to a lack of ADF rotaries)
ADF Minor Dec	4/25	L	FSX ADF 10 Dec
Gear Up	3/113	L
Gear Down		L
Flaps Up	3/81	L	Errs 3/98 3/113
Flaps Down
Speed Brake Extend	3/98	L	Errs 3/114
Speed Brake Retract
Brake	3/83
Caution Lights Dim
Caution Lights Bright
Eng Deice Off	3/66		Errs 3/83 3/98
Eng Deice On
Hydral Off	3/81		Errs 3/98 3/83
Hydra On
Stick Top Button	0/7		(need to clear cycle view)
Stick Front Button	0/6		Perhaps ATC Menu 1
Collective Lights Fwd	0/4	F	Landing Lights Set /1 /0
Collective Lights Both	0/5	F	Landing Lights Set /2 /1
Collect Lights Off
Coll Gov Inc	0/2	F	Increase Helo Beep /0 /0 Errs 0/32
Coll Gov Dec	0/3	F	Decrease Helo Beep /0 /0
Collective Starter	0/0
OH Start	3/28	F	DODOSIM Generator Switch /1 /0
OH Gen
OH Batt Off
OH Bat On	3/27	F	DODOSIM Master Battery Set /1 /0
OH Avionics Off
OH Avionics On
OH Pitot Heat Off
OH Pitot Heat On
Dir Gyro Off
Dir Gyro On	3/26	F	Dir Gyro Set /1 /0
Diff 1	INOP
Diff 2	3/7	F	DODOSIM Difficulty /2
Diff 3	3/8	F	DODOSIM Difficulty /3
Diff 4	3/9	F	DODOSIM Difficulty /4
Diff 5	3/10	F	DODOSIM Difficulty /5
Heat
Heat – off
Heat – Vent on	3/11	F	DODOSIM Hydraulic Set /1/0
Heat - Heat	3/12
GEN Field Close	3/24	F	DODOSIM Gen Field Set /1 /0
GEN Field Open
GEN Reset Close	3/25	F	DODOSIM Gen Reset Set /1 /0
GEN Reset Open
Pos Light Off
Pos Light On
Anti-Coll Light off
Anti-Coll Light On
Fuel Boost Aft Close	3/23	F	DODOSIM Fuel Pump 2 /1 /0
Fuel Boost Aft Open
Fuel Boost Fwd Close	3/22	F	DODOSIM Fuel Pump 1 /1 /0
Fuel Boost Fwd Open

Todos
Separate collective from electronics - look at db15s for all connectors then can swap
Cable pedals from under floor
Explore mat options
Update document
Paint black bolt heads
Approach
Ceiling down
Paint outer back first
Sanding with vacuum
Roof consider different color from outer
Determine how to power down lights consider replacing PCB WITH RED/white array running @ 12v with internal resistors
Post completion look at 3d printing coupler for flight link control heads
Cut circles out to plug overhead headphone socket locations laser out centres to run bolt through
Test throttle assembly with KingAir
Find switch with screw able top for landing light
Mouser 7105TZQE
Mom-on-mon flaps and speed brake
Consider how to mount cougar throttle and stick
Longer term todos
Radios using Pete Bodnar encoders
Removal of JetRanger physical panel overlay for other aircraft

# Sound System

PILOT PA400S Stereo 4 Place Portable Intercom

The audio in/out cable, when plugged into the "recorder out" socket allows the intercom audio, including any ATC transmissions, to be recorder on a suitable recording device. When plugged into the "recorder in" socket, the audio in/out cable allows the playing of stereo music or other audio entertainment over the intercom audio.
The on/off press button to the right of the squelch knob is used to turn on and off the red back lighting for use at night. The back lighting should be left off whenever practical as it consumes battery power.
Please note, that as an added battery saving feature, the PA400S is automatically switched off when the pilot’s phone plug is removed.
Distributed by www.pilotcommunications.com.au, Ozcomm Australia

# FSX Data flows for radios and lights

# Data Flows

DCS
SOIC
Server
USB I/O 1
USB I/O 2
USB I/O 3
CDU

bne-dcs-soic-cmd-lineconverter
Brydling
Leo Bodnar
bne-ocr-oled
bne-dcs-joystick-to-command
Arduino
I2C Splitter
bne-dcs-gps-sender
bne-arduino-multi-oled-receiver
GPS
Oled 1
Oled 2..
Oled ..6
Oled 7

Dimmable
Simmeters
Workspace

Simmeters
Gauges

# Data Flows with Protocol and Ports

DCS
SOIC
Server
USB I/O 1
USB I/O 2
USB I/O 3
CDU

bne-dcs-soic-cmd-lineconverter
Brydling
Leo Bodnar
bne-ocr-oled
bne-dcs-joystick-to-command
Arduino
I2C Splitter
bne-dcs-gps-sender
bne-arduino-multi-oled-receiver
GPS
Oled 1
Oled 2..
Oled ..6
Oled 7

Dimmable
Simmeters
Workspace

Simmeters
Gauges

TCP-8092
UDP -7777
UDP -7780
UDP -7781
UDP -7782
COM4
Memory Scan
UDP 6061
UDP -7780
SlimDX
SlimDX
COM?
DX
DX
UDP -7781

# Devices

12V-24V
Inverter
12V LED - Relay
Fire Handle - 1
Magnetic
Switch – 1
L - Pitch
Magnetic
Switch – 2
R - Pitch
Magnetic
Switch – 3
L - Yaw
Magnetic
Switch – 6
EAC
Magnetic
Switch – 5
Anti-Lock
Magnetic
Switch – 4
R - Yaw
Fire Handle - 2
Fire Handle - 3
Landing Gear Light - 1

Engine Cluster
Altimeter
VSI
ADI
HSI
Flaps
Flood-lighting
Control - A
Back-lighting
Control - A
Rudder Pedals

I2C Demux
2 * 16 OLED
VHF-AM
2 * 16 OLED
VHF FM
2 * 16 OLED
UHF
2 * 16 OLED
ILS
2 * 16 OLED
CSMC
2 * 20 OLED
CSMP
2 * 16 OLED
TACAN
Arduino
Thrustmaster
Warthog
OC CDU
Leo Bodnar BBI-32
Brydling
OC USB Output -3
OC USB Output -2
OC USB Output -1
Non-Dimmable
Thrustmaster
R-MFD
Thrustmaster
L-MFD

# I2C Demux Schematic