Pete’s F16 Pit

## Test

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Backlighting	Ordered
Wired
Knobs mounted
Inputs Tested
Outputs Tested
Protective Coat Applied

	Poles	Switch type	Positions

EPU GEN	2	toggle	off-on
PROBE HEAT	3	toggle	on-off-on
FIRE & OHEAT DETECT	2	push	off-(on)
OXY	2	toggle	off-on
MAL & IND LTS	2
A B C D	0	indicator light	none
TEST MAINT	3	locking toggle	on-off-on

Notes:
Consider hard wiring indicators to on when power is available.
## Anti-G

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Postion names	Notes	Callback

test	2	push	off-(on)	Test

## Flt control
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions

DIGITAL	2	locking toggle	[off]-[on]
ALT FALPS	2	locking toggle	[off]-[on]
MANUAL TF FLYUP	2	locking toggle	[off]-[on]
LE FLAPS	2	locking toggle	[off]-[on]
FLCS	2	momentary toggle	(on)-off
BIT / OFF	2	locking toggle	[off]-[on]
RUN FAIL	0	indicator light	none

	J4
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	L_FLT
7	FLP_EXT
8	LEF_LCK
9	9 OPEN
10	10 OPEN

## Manual Trim

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Call Back	Pole Totals	Switch type	Positions	Position names	Notes	Callback
			1
Pitch Trim	1	0	0	encoder with center detent	thumbwheel		light stripe showing position	BMS analog axis or SimTrimNoseUp, SimTrimNoseDown
Roll Trim	1	0	0	encoder with center detent	thumbwheel		light stripe showing position	BMS analog axis or SimTrimRollLeft, SimTrimRollRight
Yaw Trim	1	0	0	encoder with center detent	thumbwheel		light stripe showing position	BMS analog axis or SimTrimYawLeft, SimTrimYawRight
Trim /AP DISC	2	1	1	locking toggle	[off]-[on]	norm, disc		SimTrimAPNORM, SimTrimAPDISC

	J30
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	ROLL
7	PITCH
8	8 OPEN,
9	ANA_PWR
10	ANA_GND
11	APITCH
12	AROLL
13	AYAW
14	YLEFT
15	YRGHT
16	RLEFT
17	RRIGHT
18	NSEUP
19	NSEDWN
20	AP_DISC

## Fuel
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback

MASTER	2	guarded toggle	off-on	OFF, MASTER	Guarded in MASTER	SimMasterFuelOff, SimMasterFuelOn
TANK INERTING	2	toggle	off-on	OFF-TANK INERTING ??????
ENG FEED	4	rotary knob	on-on-on-on	OFF, NORM, AFT, FWD	(4x45 deg)	SimFuelPumpOff, SimFuelPumpNorm, SimFuelPumpAft, SimFuelPumpFwd
AIR REFUEL	2	toggle	off-on	CLOSE, OPEN		SimFuelDoorOpen, SimFuelDoorClose?

	J6
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	FUEL_ON
7	PMP_OFF
8	PMP_NRM
9	PMP_AFT
10	PMP_FWD
11	FUL_DOR
12	12 OPEN,
13	13 OPEN,
14	14 OPEN,
15	15 OPEN,
16	16 OPEN

## Aux Comm

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback

MASTER	5	Rotary knob	on-on-on-on-on	off, STBY, LOW, NORM, EMER	(5x36 deg)	SimToggleAuxComMaster
M-4 CODE	3	locking toggle	[on]-[off]-[on]	hold, a/b, zero
CNI	2	Rotary knob	on-off	BACK UP, UFC	(2x36 deg)	SimAuxComBackup, SimAuxComUFC
REPLY	3	locking toggle	[off]-[on]-[on]	OUT, A, B
MONITOR	2	toggle	off-on	OUT, AUDIO
TACAN	3	toggle	on-off-on	A/A TR-REC-T/R		SimTACANAATR, SimTACANTR
CHANNEL 100's	10	encoder	cw/ccw	0-9 inclusive		SimCycleLeftAuxComDigit, SimDecLeftAuxComDigit
CHANNEL 10's	10	encoder	cw/ccw	0-9 inclusive		SimCycleCenterAuxComDigit, SimDecCenterAuxComDigit
CHANNEL 1's	10	encoder	cw/ccw	0-9 inclusive		SimCycleRightAuxComDigit, SimDecRightAuxComDigit
channel x/y	2	encoder	cw/ccw	x, y		SimCycleBandAuxComDigit

	J7
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	COM_OFF
7	COM_STB
8	COM_LOW
9	COM_NO
10	COM_BCK
11	COM_UFC
12	TCN_ATR
13	TCN_NTR
14	14 OPEN,
15	15 OPEN,
16	16 OPEN

	J8
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	R_GND
7	INC_LFT
8	DEC_LFT
9	INC_CEN
10	DEC_CEN
11	INC_RGHT
12	DEC_RGHT
13	INC_BND
14	DEC_BND
15	15 OPEN,
16	16 OPEN

## Ext Lighting

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes

Form	0	potentiometer	increase clockwise
Master	2	toggle	[off]-[on]	off, norm	SimExtlMasterOff, SimExtlMasterNorm
Aerial Refueling	0	potentiometer	increase clockwise
Anti Collision	2	toggle	off-on	off, anti collision	SimAntiCollOff, SimAntiCollOn
Flash Steady	2	toggle	on-off	flash, steady	SimLightsFlash, SimLightsSteady
Wing Trail	3	toggle	on-off-on	dim, off, brt	SimWingLightOff, SimWingLightBrt
Fuselage	3	toggle	on-off-on	dim, off, brt

	J9
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	EXTM_ON
7	ACOL_ON
8	FLSH_ON
9	WNG_DM
10	WNG_BRT
11	P_MSTR
12	P_DIM
13	P_CMN
14	14 OPEN,
15	15 OPEN,
16	16 OPEN

## EPU
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1	Lightbits2

EPU	3	guarded toggle	off-on-on	OFF-NORMAL-ON	Center guard on NORMAL	SimEpuOff,SimEpuAuto,SimEpuOn
RUN light	0	indicator light	none	green light				EPUOn = $100000
HYDRAZN-AIR	0	indicator light	none	HYDRAZN-AIR				Hydrazine = $100,Air = $200

	J10
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	EPU_ON
7	HYDRA
8	AIR
9	EPU_OF
10	EPU_ON

## Elect
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1	Lightbits2

MAIN PWR	3	Locking toggle	[off]-[on]-[on]	OFF, BAT, MAIN PWR		SimMainPowerOff,SimMainPowerBatt,SimMainPowerMain
CAUTION RESET	2	push	off-(on)			SimWarnReset?
FLCS PMG-MAIN GEN	0	indicator light	none	FLCS PMG-MAIN GEN				FlcsPmg = $1,MainGen = $2
STBY GEN	0	indicator light	none	STBY GEN				StbyGen = $4
EPU GEN-EPU / PMG	0	indicator light	none	EPU GEN-EPU / PMG				EpuGen = $8,EpuPmg = $10
FAIL	0	indicator light	none	FAIL				BatFail = $80
TO FLCS-FLCS RLY	0	indicator light	none	TO FLCS-FLCS RLY				ToFlcs = $20,FlcsRly = $40

	J17
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	FLCSPMG
7	MAINGEN
8	STBYGEN
9	EPUGEN
10	EPUPMG
11	BATFAIL
12	TOFLCS
13	FLCSRLY
14	PWR_OFF
15	PWRMAIN
16	WRN_RST

## AVTR

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1	Lightbits2	Lightbits3	HSIbits

AVTR	3	toggle	on-off-on	on, auto, off		SimAVTRSwitchOff, SimAVTRSwitchAuto, SimAVTRSwitchOn
					(4x45 deg)					AVTR = $2000

	J16
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	AVTR
7	AVT_OFF
8	AVT_ON
9	9 OPEN
10	10 OPEN

## ECM

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names

OPR	3	toggle	off-on-on	OFF-STBY-OPR
DIM	3	rotary	on-on-on	1, 2, 3
XMIT	2	locking toggle	[on]-[off]	xmit, blank
RESET	2	toggle	(on)-off	reset, blank
BIT	2	toggle	(on)-off	bit, blank
1	0	indicator light	none	S, A, F, T light in corners
2	0	indicator light	none	S, A, F, T light in corners
3	0	indicator light	none	S, A, F, T light in corners
4	0	indicator light	none	S, A, F, T light in corners
5	0	indicator light	none	S, A, F, T light in corners
ALT	0	indicator light	none	S, A, F, T light in corners
FRM	0	indicator light	none	S, A, F, T light in corners
SPL	0	indicator light	none	S, A, F, T light in corners

## Jet Start

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Callback	Notes	Lightbits2

JET FUEL	3	locking toggle	[on]-[off]-[on]	START2-OFF-START1	SimJFSStart	solenoid pulls to center after start ??
ENG CONT	2	guarded toggle	off-on	SEC-PRI		guarded up to PRI
AB RESET	3	toggle	(on)-off-(on)	ENG DATA-NORM-AB DATA
MAX POWER	2	locking toggle	[off]-(on)	OFF-MAX POWER
RUN	0	indicator light	none	green light			JFSOn = $200000

	J13
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	JFS_ON_LGHT
7	JFS_ON_SOL
8	JFS_ST
9	9 OPEN,
10	10 OPEN

## Audio2

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes

INTERCOM	0	potentiometer	increase clockwise
TACAN	2	potentiometer 10k log	[off]-increase clockwise		rotary pot with off switch
ILS	2	potentiometer 10k log	[off]-increase clockwise		rotary pot with off switch
HOT MIC	3	toggle	on-off-on	CIPHER, OFF, HOT MIC

## Audio

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback

COMM 1 volume	2	potetiometer	off-increase clockwise		rotary pot with off switch	BMS analog axis or SimStepComm1VolumeDown, SimStepComm1VolumeUp
COMM 1 selector	3	rotary knob	on-on-on	OFF-SQL-GD	PUSH FOR TONE,(3x45 deg)
COMM 2 volume	2	potetiometer	off-increase clockwise		rotary pot with off switch	BMS analog axis or SimStepComm2VolumeDown, SimStepComm2VolumeUp
COMM 2 selector	3	rotary knob	on-on-on	OFF-SQL-GD	PUSH FOR TONE,(3x45 deg)
SECURE VOICE	0	potetiometer	increase clockwise
TF	0	potetiometer	increase clockwise
MSL	0	potetiometer	increase clockwise			BMS analog axis or SimStepMissileVolumeDown, SimStepMissileVolumeUp
THREAT	0	potetiometer	increase clockwise			BMS analog axis or SimStepThreatVolumeDown, SimStepThreatVolumeUp

	J31
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	ANA_PWR
7	ANA_GND
8	ACM1_V
9	ACM2_V
0	AMSL_V
1	ATHRT_V
2	CM1_UP
3	CM1_DWN
4	CM2_UP
5	CM2_DWN
6	MSL_UP
7	MSL_DWN
8	THRT_UP
9	THRT_DWN
20	R_GND

## UHF
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback

UHF	4	rotary	on-on-on-on	OFF-MAIN-BOTH-ADF
TONE	2	push	off-(on)	tone
VOL	0	potentiometer	clockwise to increase
SQUELCH	2	toggle	off-on	OFF-ON
MANUAL	3	rotary	on-on-on	MANUAL-PRESET-GUARD
Freq 100's	4	encoder	cw-ccw	A, 3, 2, T
Freq 10's	10	encoder	cw-ccw	0-9 inclusive
Freq 1's	10	encoder	cw-ccw	0-9 inclusive
Freq 1/10's	10	encoder	cw-ccw	0-9 inclusive
Freq 1/1000's	4	encoder	cw-ccw	00, 25, 50, 75
CHAN	20	encoder	cw-ccw	1-19 inclusive		SimCycleRadioChannel, SimDecRadioChannel
EMB	2	push	off-(on)	??

## Manual Pitch
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback

MANUAL PITCH	2	toggle	off-on	OVRD-NORM	Horizontal wire guard loops above and below toggle	SimMPO

	J3
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT,
5	GND LEFT
6	MPTCHO NET49_1,
7	7 OPEN,
8	8 OPEN,
9	9 OPEN,
10	10 OPEN

## Threat Warn Aux
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1	Lightbits2

Search	2	on/off lighted push	off-on	search		SimRWRSetSearch		AuxSrch = $1000
activity power	2	on/off lighted push	off-on	activity power				AuxAct = $2000
Low priority	2	on/off lighted push	off-on	low		SimRWRSetGroundPriority?		AuxLow = $4000
system power	2	on/off lighted push	off-on	power		SimRwrPower		AuxPwr = $8000
fuse	0	fuse holder	none	n/a
Dimmer	0	potentiometer	rotary	n/a	no EPIC connection

	J22
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	AXSCH
7	AXACT
8	AXLOW
9	AXPWR
10	R_SRCH
11	R_GND
12	R_PWR
13	13 OPEN,
14	14 OPEN,
15	15 OPEN,
16	16 OPEN

## CMDS
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback

RWR	2	toggle	off-on	off, on		SimEWSRWROn, SimEWSRWROff
JMR	2	toggle	off-on	off, on		SimEWSJammerOn, SimEWSJammerOff
MWS	2	toggle	off-on	off, on
01	2	toggle	off-on	off, on
02	2	toggle	off-on	off, on
CH	2	toggle	off-on	off, on		SimEWSChaffOff, SimEWSChaffOn
FL	2	toggle	off-on	off, on		SimEWSFlareOff, SimEWSFlareOn
JETT	2	locking toggle	off-on	off, JETT
PRGM	5	rotary	on-on-on-on-on	bit, 1, 2, 3, 4, 5	(5x36 deg)	SimEWSProgOne, SimEWSProgTwo, SimEWSProgThree, SimEWSProgFour
MODE	6	rotary	on-on-on-on-on-on	off, stby, man, semi, auto, byp	(6x30 deg)	SimEWSModeOff, SimEWSModeStby, SimEWSModeMan, SimEWSModeSemi, SimEWSModeAuto,
STATUS NO GO	0	green indicator light	n/a	NO GO (green lit legend)
STATUS GO	0	green indicator light	n/a	GO (green lit legend)
STATUS READY	0	green indicator light	n/a	READY TO DISPENSE (green lit legend)

	J21
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	GO NET5_2,
7	NO_GO
8	RDY_DISP
9	CHAFF_LO
10	FLARE_LO

	J23
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	RWR_ON
7	JMR_ON
8	CHF_ON
9	FLR_ON
10	PRG_BIT
11	PRG_1
12	PRG_2
13	PRG_3
14	PRG_4
15	MDEOFF
16	MDESTBY
17	MDEMAN
18	MDESEMI
19	MDEAUTO
20	MDEBYP

## Gear Panel
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1	Lightbits2	Lightbits3

Emergency jettison	2	guarded push	off-(on)	n/a	breakable cover over	SimEmergencyJettison
wheel lights	0	3 x green lights	none	n/a					NoseGearDown = $10000,LeftGearDown = $20000,RightGearDown = $40000
Hook	2	lever locking toggle	[off]-[on]	dn, up		SimHookUp,SimHookDown
Ground jettison	2	locking toggle	[off]-[on]	off, enable		SimGndJettOn, SimGndJettOff
Brakes	2	toggle	off-on	chan 2, chan 1
Parking brake	3	locking toggle	[off]-[on]-[on]	off, anti skid, brake		SimParkingBrakeOff, ,SimParkingBrakeOn
Stores	2	toggle	off-on	cat III, cat I		SimCATIII,SimCATI
Horn silencer	2	push	off-(on)	n/a		SimSilenceHorn
Landing lights	3	locking t handle toggle	[on]-[off]-[on]	taxi, off, landing		SimLandingLightOn, SimLandingLightOff
Down lock release	2	push	off-(on)	n/a
Gear down enable	2	push	off-(on)	n/a	mounted on the arm of the gear handle
Gear handle	2	lollipop lever	off-on	(down and up)		AFGeapUp, AFGearDown
Gear warning light	0	yellow light	none	n/a	mounted in lollipop end of the gear handle			GEARHANDLE = $40000000

	J29
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	N_GEAR
7	L_GEAR
8	R_GEAR
9	G_HNDLE
10	PK_SOLND
11	HOOK
12	GNDJETT
13	PARKBRK
14	EMG_JET
15	CAT_III
16	L_TAXI
17	L_LAND
18	L_GEAR
19	HRN_SIL
20	20 OPEN

## MISC
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1	Lightbits2

RF quiet	3	locking toggle	[on[-[off]-[on]	silent, rf norm		SimRFNorm, SimRFQuiet, SimRFSilent
ECM light	0	green light	none	n/a				EcmPwr = $10000?
Laser arm	2	locking toggle	[off]-[on]	off, arm		SimLaserArmOn, SimLaserArmOff
Alternate release	2	push	off-(on)	n/a		SimPickle
Master arm	3	locking toggle	[on]-[off]-[on]	simulate, off, arm		SimSimMasterArm, SimSafeMasterArm, SimArmMasterArm
ADV mode	0	indicator light tile	none	active/standby
Autopilot pitch	3	locking toggle	[on]-[off]-[on]	att hold, a-p off, alt hold		SimRightAPDown, SimRightAPMid, SimRightAPUp
Autopilot roll	3	toggle	on-off-on	strg sel, att hold, hdg sel		SimLeftAPDown, SimLeftAPMid, SimLeftAPUp

	J17
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	ECM_PWR
7	AP_ON
8	TFR_STDBY
9	ECM_PWR
0	TFR_ENGAGED
1	RF_NRM
2	RF_SILNT
3	LSR_ON
4	S_PICKLE
5	MST_ARM
6	MST_SIM
7	RAP_DWN
8	RAP_UP
9	LAP_DWN
10	LAP_UP

## Threat Warn Prim
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Notes	Callback	Lightbits1	Lightbits2

Handoff	2	push	off-(on)	Green illumination on push to select handoff mode	SimRWRHandoff		HandOff = $1
Priority	2	push	off-(on)	Green illumination on push to select priority threat mode	SimRWRSetPriority		PriMode = $4
Target separate	2	push	off-(on)	Green illumination on push to separate target symbols	SimRWRSetTargetSep		TgtSep = $20
Missile Launch	0	indicator light tile	none	Red light			Launch = $2
system test	2	push	off-(on)	Green light on push
Unknown/naval	2	push	off-(on)	Green light on push	SimRWRSetNaval, SimRWRSetUnknowns		Naval = $8,Unk = $10

	19
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	HANDOFF
7	PRIMODE
8	TGTSEP
9	LAUNCH
10	NAVAL
11	UKNOWN
12	RHANDOFF
13	RSETPRI
14	RSETTGT
15	RSETNVL
16	RSETUN

## Eyebrow Lights L
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1
Left
IFF	2	push	off-(on)	IFF IDENT
Blank 1	2	push	off-(on)	(directly above IFF button)
Blank 2	2	push	off-(on)	(directly below TF-FAIL button)
TF fail	0	red indicator light	none	TF-FAIL	Red illumination, normally off		TF = $2
F-ACK	2	push	off-(on)	F-ACK		SimICPFAck
Master Caution	2	push	off-(on)	Master Caution push to reset		ExtinguishMasterCaution	MasterCaution = $1

	J16
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	TFF
7	M_CAUT
8	F_ACK
9	EXT_CTN
10	10 OPEN

## Eyebrow Lights R
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1

Right
Engine fire	2	push	off-(on)	ENGFIRE ENGINE	Red illumination, normally off		ENG_FIRE = $20, ENGINE=80000000
Fluid pressure warning	2	push	off-(on)	HYD/OIL PRESS	Red illumination, normally off		HYD = $80, / OIL = $100
Flight controls warning	2	push	off-(on)	FLCS DBU ON	Red illumination, normally off
Landing configuration	2	push	off-(on)	TO/LDG CONFIG	Red illumination, normally off		T_L_CFG = $800
Canopy seal warning	2	push	off-(on)	CANOPY	Red illumination, normally off		CAN = $400

	J11
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	E_FIRE
7	ENGINE
8	OIL
9	TL_CFG
10	CANOPY

A little challenge here as Leo provides support for more Light BITS, and Mike’s Right Eyebrow is different to what I’d been working off. Ended up using http://www.scribd.com/doc/903695/F16MLU-Checklist as a reference

	Original	Mike	F4IM	F4IM Comments
Engine	7	Engine		ENG_FIRE	6
E_Fire	6	Eng Fire		ENG_FIRE	6
OIL	8	Press		OIL	7
		HYD/OIL		HYD	8
		FLCS		DUAL	9
		DBO ON		DUAL	9
TL_CFG	9	TO/LDG		T_L_CFG	10
		CONFIG		CONFIG	11
Canopy	10	CANOPY		CAN	12
		OXY LOW	N/A

As Wired
		1	2	3	4	5	6	7	8
ENG FIRE	1	X
ENGINE	2		X
PRESS	3			X
CONFIG	4				X
CANOPY	5					X
HYD/OIL	6			X
DBU ON	7						X
FLCS	8							X
TO/LDG	9				X
OXY LOW	10								X

ENG FIRE / 1	HYD/OIL / 6	FLCS / 8	TO/LDG / 9	CANOPY / 5
ENGINE / 2	PRESS / 3	DBU ON / 7	CONFIG / 4	OXY LOE / 10

Final Wiring of Spare Connector
	J32
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	E_FIRE
7	ENGINE
8	OIL
9	TL_CFG
10	CANOPY
11	FLCS
12	DBU ON
13	OXY LOW

Indexer L

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1

Left Indexer
							AOAAbove = $1000
							AOAOn = $2000
							AOABelow = $4000

	J8
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	A_ABVE
7	A_ON
8	A_BLOW
9	9 OPEN,
10	10 OPEN

## Indexer R

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	Poles	Switch type	Positions	Position names	Notes	Callback	Lightbits1

Right Indexer
							RefuelRDY = $8000
							RefuelAR = $10000
							RefuelDSC = $20000

	J9
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	R_RDY NET41_2,
7	R_AR NET40_2,
8	R_DSC NET39_2,
9	9 OPEN,
10	10 OPEN

## ICP

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Position names	Notes	Callback

COM1	2	push	off-(on)	n/a		SimICPCom1
COM2	2	push	off-(on)	n/a		SimICPCom2
IFF	2	push	off-(on)	n/a		SimICPIFF
LIST	2	push	off-(on)	n/a		SimICPLIST
A-A	2	push	off-(on)	n/a		SimICPAA
A-G	2	push	off-(on)	n/a		SimICPAG
1 key	2	push tile	off-(on)	n/a		SimICPTILS
2 key	2	push tile	off-(on)	n/a		SimICPALOW
3 key	2	push tile	off-(on)	n/a		SimICPTHREE
Recall key	2	push tile	off-(on)	n/a		SimICPCLEAR
4 key	2	push tile	off-(on)	n/a		SimICPStpt
5 key	2	push tile	off-(on)	n/a		SimICPCrus
6 key	2	push tile	off-(on)	n/a		SimICPSIX
enter key	2	push tile	off-(on)	n/a		SimICPEnter
7 key	2	push tile	off-(on)	n/a		SimICPMark
8 key	2	push tile	off-(on)	n/a		SimICPEIGHT
9 key	2	push tile	off-(on)	n/a		SimICPNINE
0 key	2	push tile	off-(on)	n/a		SimICPZERO
WX	2	push	off-(on)	n/a
ICP inc/dec	3	rocker	(on)-off-(on)	down arrow, up arrow		SimICPNext, SimICPPrevious
display control switch	4	4-way momentary bat	(on)-(on)-(on)-(on)-center off	down, rtn, up, seq (cw from bottom)	?	SimICPDEDDOWN, SimICPResetDED ,SimICPDEDUP, SimICPDEDSEQ
Drift cutoff	3	toggle (momentary 1 side only)	(on)-off-on	warn reset, norm, drift c/o		SimDriftCOOff, SimDriftCOOn
FLIR up/down	3	rocker	(on)-off-(on)	down arrow, up arrow
FLIR gain	3	toggle	on-off-on	auto, lvl, gain
SYM	2	10k linear pot	off-increase clockwise	off		BMS analog axis or SimSymWheelD <SimSymWheelUp
BRT	0	10k linear pot	off-increase clockwise			BMS analog axis or SimHUDBrightnessDown, SimHUDBrightnessUp
						SimHUDOn, SimHUDOff
RET DEPR	0	10k linear pot	increase clockwise			BMS analog axis or SimRetDn,SimRetUp
CONT	0	10k linear pot	increase clockwise

## INSTR

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

mode	4	rotary	on-on-on-on	ils/tcn, tcn, nav, ils/nav	(4x30 deg)	SimHSIIlsTcn, SimHSITcn, SimHSINav, SimHSIIlsNav
heading	0	potentiometer	rotary	n/a	no EPIC connection

	J4	Implemented
1	BKLGT-V	BKLGT-V
2	BKLGT+V	BKLGT+V
3	+12V	+12V
4	+28V	+28V
5	GND ,	GND ,
6	I_TCN	I_TCN
7	TCN	TCN
8	NAV	I_NAV
9	I_NAV	OPEN
10	10 OPEN,	OPEN
11	R_GND	R_GND
12	R_CRSE_A	R_CRSE_HEAD_A
13	R_CRSE_B	R_CRSE_HEAD_A
14	R_HEAD_A	R_Pushed
15	R_HEAD_B
16	16 OPEN

## HIS – Not used

Build Status - not used
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback
course	360	encoder	rotary	n/a		SimHsiCourseDec, SimHsiCourseInc
heading	360	encoder	rotary	n/a		SimHsiHeadingDec, SimHsiHeadingInc

The Course and Heading input is mapped to a single rotary on the INSTR panel, with the role changing if the rotary is pushed while rotating.
## Fuel Qty Select

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

source	6	rotary	on-on-on-on-on-on	ext ctr, ext wing, int wing, rsvr, norm, test	(6x45 deg)	SimFuelSwitchCenterExt, SimFuelSwitchWingExt, SimFuelSwitchWingInt, SimFuelSwitchResv, SimFuelSwitchNorm, SimFuelSwitchTest
Fuel transfer	2	locking toggle	[off]-[on]	wing first, norm		SimFuelTransWing,SimFuelTransNorm

	J12
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	MARKER
7	EXT_WNG
8	INT_WNG
9	RVSR
10	NORM
11	TEST
12	TRNSFR
13	EXT_CTR
14	INST_FLG1
15	INST_FLG2
16	INST_FLG3

## Caution Panel

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Lightbits1	Lightbits2	Lightbits3
CONFIG = $40
DUAL = $200;
FltControlSys = $40000
LEFlaps = $80000
EngineFault = $100000
Overheat = $200000
FuelLow = $400000
Avionics = $800000
RadarAlt = $1000000
IFF = $2000000
ECM = $4000000
Hook = $8000000
NWSFail = $10000000
CabinPress = $20000000
	FwdFuelLow = $40000
	AftFuelLow = $80000
	SEC = $400000
	OXY_LOW = $800000
	PROBEHEAT = $1000000
	SEAT_ARM = $2000000
	BUC = $4000000
	FUEL_OIL_HOT = $8000000
	ANTI_SKID = $10000000
		Elec_Fault = $400

## Sensor Power

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes

Left hardpoint	2	toggle	off-on	off, left hdpt	SimLeftHptOff, SimLeftHptOn
Right hardpoint	2	toggle	off-on	off, right hdpt	SimRightHptOff, SimRightHptOn
Fire control radar	2	toggle	off-on	off, fcr	SimFCROff, SimFCROn
Radar altimeter	3	toggle	off-on-on	off, stby, rdr alt	SimRALTOFF, SimRALTSTDBY, SimRALTOFF

	J23
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	L_HPT
7	R_HPT
8	FCR
9	RA_STD
10	RA_ON

## HUD Control

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

Velocity scales	3	toggle	off-on-on	off, vah, vv/vah		SimScalesOff, SimScalesVAH, SimScalesVVVAH
Attitude scales	3	toggle	off-on-on	off, fpm, att/fpm		SimPitchLadderOff, SimPitchLadderFPM, SimPitchLadderATTFPM
Data Entry	3	toggle	off-on-on	off, pfl, ded data		SimHUDDEDOff, SimHUDDEDPFL, SimHUDDEDDED
DEPR reticle	3	toggle	[off]-[on]-[on]	off, pri, stby		SimReticleOff, SimReticlePri, SimReticleStby
Velocity	3	toggle	off-on-on	gnd spd, tas, cas		SimHUDVelocityGND, SimHUDVelocityTAS, SimHUDVelocityCAS
Altitude	3	toggle	off-on-on	auto, baro, alt radar		SimHUDAltAuto, SimHUDAltBaro, SimHUDAltRadar
Brightness	3	toggle	off-on-on	night, auto, day		SimHUDBrtNight, SimHUDBrtAuto, SimHUDBrtDay
Test	3	toggle	off-on-on	off, on, test step

1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	S_VA
7	S_VV
8	FPM
9	AT_FPM
10	PFL
11	DED
12	R_PRI
13	R_STD
14	A_BARO
15	A_RDR
16	NIGHT
17	DAY
18	CAS
19	GNDSPD
20	20 OPEN

## Nuclear consent

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names

plain	2	toggle	off-on	crad1, crad 2
arm	3	guarded toggle	on-off-on	rel only, off, arm rel

## Lighting

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names

Consoles (primary)	0	potentiometer	increase clockwise
instrument panel (primary)	0	potentiometer	increase clockwise
Data entry display (primary)	0	potentiometer	increase clockwise
Consoles (flood)	2	off-potentiometer	increase clockwise
instrument panel (flood)	0	potentiometer	increase clockwise
malfunction lights	2	toggle	off-on	dim, brt

	J27
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	POT_GND POT_GROUND_4,
7	POT_+V POT_+V_4,
8	POT_1 POT_1_4,
9	POT_2 POT_2_4,
10	POT_3 POT_3_4,
11	POT_4 POT_4_4,
12	DIM_BRIGHT DIM_BRIGHT_4,
13	13 OPEN,
14	14 OPEN,
15	15 OPEN,
16	16 OPEN

## Master Zeroize
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

voice message	2	toggle	off-on	inhibit, voice message		SimVMSOFF, SimVMSOn
zeroize	3	guarded toggle	on-off-on	data zeroize, blank, master zeroize	guarded in center off position

	J33
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	V_INHB NET5_5,
7	7 OPEN,
8	8 OPEN,
9	9 OPEN,
10	10 OPEN

## Air Cond

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

air source	4	rotary	on-on-on-on	off, norm, dump, ram	(4x45 deg)	SimAirSourceOff, SimAirSourceNorm, SimAirSourceDump, SimAirSourceRam
temp	7	rotary	on-on-on-off-on-on-on		No EPIC connection

	J34
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	OFF
7	NORM
8	DUMP
9	RAM
10	10 OPEN

## KY-58

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes

mode	4	rotary knob	on-on-on-on	p, c, ld, rv	(4x45 deg)
volume	0	10k log potentiometer	clockwise to increase		no EPIC connection
number rotary	8	rotary knob	{on}-on-on-on-on-on-on-{on}	215, 1, 2, 3, 4, 5, 6, 7 all	(8x30 deg)
on/off rotary	3	rotary knob	on-on-on	off, on, TD	(3x30 deg)

## Avionics Power

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

FCC	2	Locking toggle	[off]-[on]	off, FCC		SimFCCOff, SimFCCOn
SMS	2	Locking toggle	[off]-[on]	off, SMS		SimSMSOff, SimSMSOn
MFD	2	Locking toggle	[off]-[on]	off, MFD		SimMFDOff, SimMFDOn
UFC	2	Locking toggle	[off]-[on]	off, UFC		SimUFCOff, SimUFCOn
INS	7	Rotary knob	on-on-on-on-on-on-on	off, stor hdg, norm, nav, cal, in flt align, att	(7x45deg)	SimINSOff, SimINSNorm, SimINSNav, SimINSInFlt
GPS	2	Locking toggle	[off]-[on]	off, GPS		SimGPSOff, SimGPSOn
DL	2	Locking toggle	[off]-[on]	off, DL		SimDLOff, SimDLOn
MAP	2	Locking toggle	[off]-[on]	off, MAP		SimMAPOff, SimMAPOn

	J24
1	BKLGT-V
2	BKLGT+V
3	+12V
4	+28V
5	GND ,
6	FCC
7	SMS
8	MFD
9	UFC
10	I_OFF
11	I_HDG
12	I_NRM
13	I_NAV
14	I_CAL
15	I_ATT
16	GPS
17	TISL
18	MAP
19	P_GND PHY_MFD_PWR_4,
20	P_MFD_PWR PHY_GND_4

## Anti-Ice

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

engine anti ice	3	locking toggle	[off]-[on]-[on]	off, auto, on
IFF antenna select	3	toggle	on-off-on	lower, norm, upper
UHF antenna select	3	toggle	on-off-on	lower, norm, upper

## Oxy Reg

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names

Flow control (red)	3	lever	on-on-on	Test mask, norm, Emer
Oxygen content (green)	2	lever	on-on	Norm, 100% O2
Pressure control (grey)	3	lever	off-on-on	off, on, PBG

## DTU

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions

DTU	2	toggle	off-on

## Left MFD

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Notes	Callback

OSB1	2	push	off-(on)		SimCBEOSB_1L
OSB2	2	push	off-(on)		SimCBEOSB_2L
OSB3	2	push	off-(on)		SimCBEOSB_3L
OSB4	2	push	off-(on)		SimCBEOSB_4L
OSB5	2	push	off-(on)		SimCBEOSB_5L
OSB6	2	push	off-(on)		SimCBEOSB_6L
OSB7	2	push	off-(on)		SimCBEOSB_7L
OSB8	2	push	off-(on)		SimCBEOSB_8L
OSB9	2	push	off-(on)		SimCBEOSB_9L
OSB10	2	push	off-(on)		SimCBEOSB_10L
OSB11	2	push	off-(on)		SimCBEOSB_11L
OSB12	2	push	off-(on)		SimCBEOSB_12L
OSB13	2	push	off-(on)		SimCBEOSB_13L
OSB14	2	push	off-(on)		SimCBEOSB_14L
OSB15	2	push	off-(on)		SimCBEOSB_15L
OSB16	2	push	off-(on)		SimCBEOSB_16L
OSB17	2	push	off-(on)		SimCBEOSB_17L
OSB18	2	push	off-(on)		SimCBEOSB_18L
OSB19	2	push	off-(on)		SimCBEOSB_19L
OSB20	2	push	off-(on)		SimCBEOSB_20L
					SimCBEOSB_GAINUP_L
30					SimCBEOSB_GAINDOWN_L

## Right MFD

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Notes	Callback

OSB1	2	push	off-(on)		SimCBEOSB_1R
OSB2	2	push	off-(on)		SimCBEOSB_2R
OSB3	2	push	off-(on)		SimCBEOSB_3R
OSB4	2	push	off-(on)		SimCBEOSB_4R
OSB5	2	push	off-(on)		SimCBEOSB_5R
OSB6	2	push	off-(on)		SimCBEOSB_6R
OSB7	2	push	off-(on)		SimCBEOSB_7R
OSB8	2	push	off-(on)		SimCBEOSB_8R
OSB9	2	push	off-(on)		SimCBEOSB_9R
OSB10	2	push	off-(on)		SimCBEOSB_10R
OSB11	2	push	off-(on)		SimCBEOSB_11R
OSB12	2	push	off-(on)		SimCBEOSB_12R
OSB13	2	push	off-(on)		SimCBEOSB_13R
OSB14	2	push	off-(on)		SimCBEOSB_14R
OSB15	2	push	off-(on)		SimCBEOSB_15R
OSB16	2	push	off-(on)		SimCBEOSB_16R
OSB17	2	push	off-(on)		SimCBEOSB_17R
OSB18	2	push	off-(on)		SimCBEOSB_18R
OSB19	2	push	off-(on)		SimCBEOSB_19R
OSB20	2	push	off-(on)		SimCBEOSB_20R
					SimCBEOSB_GAINUP_R
					SimCBEOSB_GAINDOWN_R

## Other
Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback

Chaff/flare button
Alt gear	2				?	AFAlternateGear, AFAlternateGearReset
Canopy switch	2					AFCanopyToggle
pedal adj	0	T handle	mechanical	none
Mark beacon	0	green indicator light	none	mrk bcn

## ACES-II

Build Status
Panel Purchased
Back Panel Purchased
Mounted in Pit
Wired
Knobs mounted
Inputs Tested
Outputs Tested

Switch Name	# of poles	Positions	Postion names	Notes	Callback

Eject grip	2				SimEject
Safety Lever	2				SimSeatOff, SimSeatOn
Manual release

	J15
1	BKLGT-V
2	BKLGT+V
3	+12V LEFT
4	+28V LEFT
5	GND LEFT
6	EJECT
7	SEAT_ON
8	8 OPEN,
9	9 OPEN,
10	10 OPEN

## TQS

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback
DOGFIGHT	3		on-off-on	DDOGFIGHT, ,		SimSelectMRMOverride, SimDeselectOverride, SimSelectSRMOverride
MAN RNG/UNCAGE		Rotary knob		MAN RNG/UNCAGE		BMS alanog axis or SimRangeKnobDown, SimRangeKnobUp
ANT ELEV		Rotary knob	Detented center			BMS alanog axis or SimRadarElevationDown, SimRadarElevationCenter, SimRadarElevationUp
CURSOR		Joystick				BMS alanog axes or SimCursorDown ,SimCursorLeft ,SimCursorRight , SimCursorUp
ENABLE	2	push	off-(on)			SimCursorEnable
Speed Brake	2					AFBrakesIn, AFBrakesOut
PTT	4			VHF,UHF,IFF IN,IFF OUT		SimTransmitCom2,SimTransmitCom1
Black-Out Switch	2

## SSCG

Switch Name	# of poles	Switch type	Positions	Postion names	Notes	Callback
NWS-A/R DISC-MSL STEP	2		off,(on)			SimMissileStep
Trim	5			Off,Fwd,Aft,Left,Right		AFElevatorTrimUp, AFElevatorTrimDown ,AFAileronTrimLeft, AFAileronTrimRight
Display Manag	5			Off,Fwd,Aft,Left,Right		SimDMSUp, SimDMSDown, SimDMSLeft,SimDMSRight
Weapon Release	2		off,(on)			SimPickle
Paddle Switch	2					SimAPOverride
Trigger	3			Off,Detent1,Detent2		SimTriggerFirstDetent, SimTriggerSecondDetent
Pinky Switch	2					SimPinkySwitch
TMS	5			Off,Fwd,Aft,Left,Right		SimTMSUp,SimTMSDown, SimTMSLeft,SimTMSRight
CMS	5			Off,Fwd,Aft,Left,Right		SimDropProgrammed, SimECMConsent, ,SimECMStandby

# Switch Mapping for non-Falcon
## Test
	Lomac	Postion names	Keystroke

EPU gen		off-epu gen
PROBE HEAT		test-off-probe heat
FIRE & OHEAT DETECT		n/a
OXY		off-QTY
MAL & IND LTS		n/a
A B C D
test maint		h

## Anti-G
Switch Name	Lomac	Postion names	Keystroke

Test		Test

## Flt control
Switch Name	Lomac	Postion names	Keystroke

DIGITAL		off-backup
ALT FALPS	Flaps Up	norm	LCtrl-F
	Flaps Landing Position	extend	LShift-F
MANUAL TF FLYUP		disable-enable
LE FLAPS		auto-lock
FLCS		reset-off
BIT / OFF		OFF, BIT
RUN FAIL

## Manual Trim
Switch Name	Lomac	Position names	Keystroke

Pitch Trim
Roll Trim
Yaw Trim
Trim /AP DISC		norm, disc

## Fuel
Switch Name	Lomac	Position names	Key Strokes

MASTER	Engines Stop	OFF	RShift-End
		MASTER
TANK INERTING	Fuel Dump	OFF-TANK INERTING	R
ENG FEED		OFF, NORM, AFT, FWD
AIR REFUEL	Refueling Bay	CLOSE,	LCtrl-R
		OPEN	LCtrl-R

## Aux Comm
Switch Name	Lomac	Position names	Keystroke

MASTER		off, STBY, LOW, NORM, EMER
M-4 CODE		hold, a/b, zero
CNI		BACK UP, UFC
REPLY		OUT, A, B
MONITOR		OUT, AUDIO
TACAN		A/A TR-REC-T/R
CHANNEL 100's		0-9 inclusive
CHANNEL 10's		0-9 inclusive
CHANNEL 1's		0-9 inclusive
channel x/y		x, y

## Ext Lighting
Switch Name	Lomac	Position names	Keystrokes

Form
Master	Illumination Cockpit	off	L
		norm	L
Aerial Refueling
Anti Collision	Navigation lights	Off	RCtrl-L
		anti collision	RCtrl-L
Flash Steady		flash, steady
Wing Trail	Smoke	dim, off, brt	T
		off	T
		brt	T
Fuselage		dim, off, brt

## EPU
Switch Name	Lomac	Position names	Keystroke

EPU	3	OFF-NORMAL-ON	Center guard on NORMAL
RUN light	0	green light
HYDRAZN-AIR	0	HYDRAZN-AIR

## Elect
Switch Name	Lomac	Position names	Keystrokes

MAIN PWR	Power Switch	OFF	Shift-P
		BAT	Shift-P
		MAIN PWR	Shift-P
CAUTION RESET
FLCS PMG-MAIN GEN		FLCS PMG-MAIN GEN
STBY GEN		STBY GEN
EPU GEN-EPU / PMG		EPU GEN-EPU / PMG
FAIL		FAIL
TO FLCS-FLCS RLY		TO FLCS-FLCS RLY

## AVTR
Switch Name	Lomac	Position names	Keystroke

AVTR		on, auto, off

## ECM
Switch Name	Lomac	Position names	Keystroke

OPR		OFF-STBY-OPR
DIM		1, 2, 3
XMIT		xmit, blank
RESET		reset, blank
BIT		bit, blank
1		S, A, F, T light in corners
2		S, A, F, T light in corners
3		S, A, F, T light in corners
4		S, A, F, T light in corners
5		S, A, F, T light in corners
ALT		S, A, F, T light in corners
FRM		S, A, F, T light in corners
SPL		S, A, F, T light in corners

## Jet Start
Switch Name	Lomac	Position names	Keystroke

JET FUEL	Engines Start	START2-OFF-START1	RShift-Home
ENG CONT		SEC-PRI
AB RESET		ENG DATA-NORM-AB DATA
MAX POWER		OFF-MAX POWER
RUN		green light

## Audio2
Switch Name	Lomac	Position names	Keystroke

INTERCOM
TACAN
ILS
HOT MIC		CIPHER, OFF, HOT MIC

## Audio
Switch Name	Lomac	Position names	Keystroke

COMM 1 volume
COMM 1 selector		OFF-SQL-GD
COMM 2 volume
COMM 2 selector		OFF-SQL-GD
SECURE VOICE
TF
MSL	0
THREAT	0

## UHF
Switch Name	Lomac	Position names	Keystroke

UHF		OFF-MAIN-BOTH-ADF
TONE		tone
VOL
SQUELCH		OFF-ON
MANUAL		MANUAL-PRESET-GUARD
Freq 100's		A, 3, 2, T
Freq 10's		0-9 inclusive
Freq 1's		0-9 inclusive
Freq 1/10's		0-9 inclusive
Freq 1/1000's		00, 25, 50, 75
CHAN		1-19 inclusive
EMB		??

## Manual Pitch
Switch Name	Lomac	Position names	Keystroke

MANUAL PITCH		OVRD-NORM

## Threat Warn Aux
Switch Name	Lomac	Position names	Keystroke

Search		search
activity power		activity power
Low priority		low
system power		power
fuse		n/a
Dimmer		n/a

## CMDS
Switch Name	Lomac	Position names	Keystroke

RWR		off, on
JMR		off, on
MWS		off, on
01		off, on
02		off, on
CH		off, on
FL		off, on
JETT		off, JETT
PRGM		bit, 1, 2, 3, 4, 5
MODE		off, stby, man, semi, auto, byp
STATUS NO GO		NO GO (green lit legend)
STATUS GO	0	GO (green lit legend)
STATUS READY	0

## Gear Panel
Switch Name	Lomac	Position names	Keystrokes

Emergency jettison	Weapons Jettison		LCtrl-W
wheel lights
Hook	Toggle Arrestor Hook		Ctl-G
Ground jettison
Brakes
Parking brake		off
	Wheel Brake on	anti skid	W
	Wheel Brake on	brake	W
Stores		cat III, cat I
Horn silencer	Audible Warning Reset	n/a	RShift-N
Landing lights	Gear Light Near/Far/Off	taxi	RAlt-L
	Gear Light Near/Far/Off	off	RAlt-L
	Gear Light Near/Far/Off	landing	RAlt-L
Down lock release		n/a
Gear down enable		n/a
Gear handle	Landing Gear Down	Down	LShift-G
	Landing Gear Up	Up	LCtrl-G
Gear warning light		n/a

## MISC
Switch Name	Lomac	Position names	Keystrokes

RF quiet	Radar On/Off	silent	I
		rf norm	I
ECM light		n/a
Laser arm		off, arm
Alternate release	Weapon Fire	n/a	Space
Master arm		simulate, off, arm
ADV mode		active/standby
Autopilot pitch		att hold, a-p off, alt hold
Autopilot roll		strg sel, att hold, hdg sel

## Threat Warn Prime
Switch Name	Lomac	Positions	Notes

Handoff		off-(on)
Priority		off-(on)
Target separate		off-(on)
Missile Launch		none
system test		off-(on)
Unknown/naval		off-(on)

## Eyebrow Lights L
Switch Name	Lomac	Position names	Keystrokes

IFF		IFF IDENT
Blank 1		(directly above IFF button)
Blank 2		(directly below TF-FAIL button)
TF fail		TF-FAIL
F-ACK		F-ACK	RShift-N
Master Caution		Master Caution push to reset	RShift-N

## Eyebrow Lights R
Switch Name	Lomac	Position names	Keystroke

Right
Engine fire		ENGFIRE ENGINE
Fluid pressure warning		HYD/OIL PRESS
Flight controls warning		FLCS DBU ON
Landing configuration		TO/LDG CONFIG
Canopy seal warning		CANOPY

Indexer L

Switch Name	Lomac	Position names	Keystrok

Left Indexer

## Indexer R

Switch Name	Lomac	Position names	Keystroke

Right Indexer

## ICP
Switch Name	Lomac	Position names	Keystroke

COM1		n/a
COM2		n/a
IFF		n/a
LIST		n/a
A-A		n/a
A-G		n/a
1 key		n/a
2 key		n/a
3 key		n/a
Recall key		n/a
4 key		n/a
5 key		n/a
6 key		n/a
enter key		n/a
7 key		n/a
8 key		n/a
9 key		n/a
0 key		n/a
WX		n/a
ICP inc/dec		down arrow, up arrow
display control switch		down, rtn, up, seq (cw from bottom)	?
Drift cutoff		warn reset, norm, drift c/o
FLIR up/down		down arrow, up arrow
FLIR gain		auto, lvl, gain
SYM		off
BRT

RET DEPR
CONT

## INSTR

Switch Name	Lomac	Postion names	Keystroke

mode		ils/tcn, tcn, nav, ils/nav
heading		n/a

## HIS – Not used
Switch Name	Lomac	Postion names	Keystroke
course		n/a
heading		n/a

## Fuel Qty Select
Switch Name	Lomac	Postion names	Keystroke

source		ext ctr, ext wing, int wing, rsvr, norm, test
Fuel transfer		wing first, norm

## Sensor Power
Switch Name	Lomac	Postion names	Keystroke

Left hardpoint		off, left hdpt
Right hardpoint		off, right hdpt
Fire control radar		off, fcr
Radar altimeter		off, stby, rdr alt

## HUD Control
Switch Name	Lomac	Postion names	Keystrokes

Velocity scales		off, vah, vv/vah
Attitude scales		off, fpm, att/fpm
Data Entry		off, pfl, ded data
DEPR reticle		off, pri, stby
Velocity		gnd spd, tas, cas
Altitude		auto, baro, alt radar
Brightness	HUD Colour	night	RCtrl-H
		auto	RCtrl-H
		day	RCtrl-H
Test		off, on, test step

## Nuclear consent
Switch Name	Lomac	Positions	Keystroke

plain		off-on
arm		on-off-on

## Lighting
Switch Name	Lomac	Positions	Keystroke

Consoles (primary)		increase clockwise
instrument panel (primary)		increase clockwise
Data entry display (primary)		increase clockwise
Consoles (flood)		increase clockwise
instrument panel (flood)		increase clockwise
malfunction lights		off-on

## Master Zeroize

Switch Name	Lomac	Postion names	Keystroke

voice message		inhibit, voice message
zeroize		data zeroize, blank, master zeroize

## Air Cond
Switch Name	Lomac	Postion names	Keystroke

air source		off, norm, dump, ram
temp

## KY-58
Switch Name	Lomac	Postion names	Keystroke

mode		p, c, ld, rv
volume
number rotary		215, 1, 2, 3, 4, 5, 6, 7 all
on/off rotary		off, on, TD

## Avionics Power
Switch Name	Lomac	Postion names	Keystroke

FCC		off, FCC
SMS		off, SMS
MFD		off, MFD
UFC		off, UFC
INS		off, stor hdg, norm, nav, cal, in flt align, att
GPS		off, GPS
DL		off, DL
MAP		off, MAP

## Anti-Ice
Switch Name	Lomac	Postion names	Keystroke

engine anti ice		off, auto, on
IFF antenna select		lower, norm, upper
UHF antenna select		lower, norm, upper

## Oxy Reg
Switch Name	Lomac	Postion names	Keystroke

Flow control (red)	3	Test mask, norm, Emer
Oxygen content (green)	2	Norm, 100% O2
Pressure control (grey)	3	off, on, PBG

## DTU
Switch Name	Lomac	Positions	Keystroke

DTU		off-on

## Left MFD
Switch Name	Lomac	Positions	Keystroke

OSB1		off-(on)
OSB2		off-(on)
OSB3		off-(on)
OSB4		off-(on)
OSB5		off-(on)
OSB6		off-(on)
OSB7		off-(on)
OSB8		off-(on)
OSB9		off-(on)
OSB10		off-(on)
OSB11		off-(on)
OSB12		off-(on)
OSB13		off-(on)
OSB14		off-(on)
OSB15		off-(on)
OSB16		off-(on)
OSB17		off-(on)
OSB18		off-(on)
OSB19		off-(on)
OSB20		off-(on)

## Right MFD
Switch Name	Lomac	Positions	Keystroke

OSB1		off-(on)
OSB2		off-(on)
OSB3		off-(on)
OSB4		off-(on)
OSB5		off-(on)
OSB6		off-(on)
OSB7		off-(on)
OSB8		off-(on)
OSB9		off-(on)
OSB10		off-(on)
OSB11		off-(on)
OSB12		off-(on)
OSB13		off-(on)
OSB14		off-(on)
OSB15		off-(on)
OSB16		off-(on)
OSB17		off-(on)
OSB18		off-(on)
OSB19		off-(on)
OSB20		off-(on)

## Other
Switch Name	Lomac	Positions	Keystrokes

Chaff/flare button
Alt gear
Canopy switch	Canopy Open/Close	Open	LCtrl-C
	Canopy Open/Close	Close	LCtrl-C
pedal adj
Mark beacon

## ACES-II
Switch Name	Lomac	Positions	Keystrokes

Eject grip	Eject		LCtrl-E (3 times)
Safety Lever
Manual release

## TQS

Switch Name	Lomac	Postion names	Keystroke
DOGFIGHT		DDOGFIGHT, ,
MAN RNG/UNCAGE		MAN RNG/UNCAGE
ANT ELEV
CURSOR
ENABLE
Speed Brake
PTT		VHF,UHF,IFF IN,IFF OUT
Black-Out Switch

## SSCG
Switch Name	Lomac	Postion names	Keystroke
NWS-A/R DISC-MSL STEP
Trim		Off,Fwd,Aft,Left,Right
Display Manag		Off,Fwd,Aft,Left,Right
Weapon Release
Paddle Switch
Trigger		Off,Detent1,Detent2
Pinky Switch
TMS		Off,Fwd,Aft,Left,Right
CMS		Off,Fwd,Aft,Left,Right