The following table provides a brief description of the fields present in X‑Plane 10’s Data Set screen. Note that this list is current as of X‑Plane 10.30.
In this table, note that each group of data fields is labeled as it would be in the Data Input & Output window. For instance, to see the values of the “f-act” or “frame time” variables, you would consult the table and see that those variables are under the frame ratelabel. Simply check the frame rate box in the Data Input & Output to see those variables. Alternately, if you know you want frame
rate-related variables, you could consult the portion of the table under the frame rateheading to find out what data is available. Where the meaning of a label in the Data Input & Output window is not immediately obvious, a longer version of the label is given—for instance, “Simulator statistics (sim stats).”
Field label	Descriptions of fields available in X‑Plane 10’s data output
Frame rate
f-act, /sec	The actual frame rate being displayed by X-Plane. Unless your computer is bogged down, this will be the same as f-sim.
f-sim, /sec	The frame rate the simulator is “pretending” to have in order to keep the flight model from failing.
frame, time	The time required to render one frame, in seconds.
cpu, time	•
gpu, time	•
grnd, ratio	•
flit, ratio	•
Times
real, time	The number of seconds, in the real world, elapsed since the simulator was launched.
totl, time	The number of seconds elapsed since the simulator was launched minus time spent in a loading screen.
missn, time	The time since the start of the “mission” (generally the time since the last time an aircraft or location was loaded).
timer, time	The time elapsed on a timer for general use.
zulu, time	“Zulu” time (Greenwich Mean Time, or GMT) in the simulator, in decimal hours (e.g., 3.5 for 3:30 a.m.).
local, time	Local time in the simulator, in decimal hours.
hobbs, time	The aircraft’s Hobbs time (a measurement of how long the aircraft’s systems have been run).
Simulator statistics (sim stats)
explo, DIM	•
explo, USE	•
cratr, DIM	•
cratr, USE	•
puffs, TOT	•
puffs, VIS	•
tris, vis	•
q, depth	•
Speeds
Vind, kias	The craft’s indicated airspeed, in knots indicated airspeed.
Vind, keas	The craft’s indicated airspeed, in knots equivalent airspeed (the calibrated airspeed corrected for adiabatic compressible flow at the craft’s current altitude).
Vtrue, ktas	The craft’s true airspeed (the speed of the craft relative to undisturbed air), in knots true airspeed.
Vtrue, ktgs	True airspeed, in knots true ground speed.
Vind, mph	The craft’s indicated airspeed, in miles per hour.
Vtrue, mphas	The craft’s true airspeed, in miles per hour airspeed.
Vtrue, mphgs	The craft’s true airspeed, in miles per hour ground speed.
Aircraft Mach speeds, vertical velocity, and g-loads (mach, VVI, G-load)
Mach, ratio	The aircraft’s current speed, as a ratio to Mach 1.
VVI, fpm	The aircraft’s current vertical velocity, in feet per minute. If everything is working as it should, this is normal to the local horizon under the aircraft.
Gload, norml	The g-load across the aircraft, relative to the aircraft body-axis, if all is working as it should.
Gload, axial	The axial g-load on the aircraft.
Gload, side	The side g-load on the aircraft.
Atmosphere: weather
SLprs, inHG	SLprs, in inches mercury.
SLtmp, degC	SLtmp, in degrees Celsius.
wind, speed	The wind speed around the aircraft, in knots.
wind, dir	The wind direction, in degrees clockwise deviation from north. Wind blowing from north to south has direction 0.0, while wind blowing from west to east has direction 270.0.
trb, locl	Amount of local turbulence.
prec, locl	Amount of local precipitation.
hail, locl	Amount of local hail.
Atmosphere: aircraft
AMprs, inHG	AMprs, in inches mercury.
AMtmp, degC	AMtmp, in degrees Celsius.
LEtmp, degC	LEtmp, in degrees Celsius.
dens, ratio	The aircraft’s density ratio.
A, ktas	A, in knots true airspeed.
Q, psf	Q, dynamic pressure or velocity pressure, in pounds per square foot.
gravi, fts2	Gravitational force, in feet per second squared.
System pressures
baro, inHG	Barometric pressure, in inches mercury.
edens, part	•
vacum, ratio	•
elec, ratio	•
AHRS, ratio	Pressure in the attitude heading reference system (AHRS), as a ratio to normal.
Joystick aileron, elevator, and rudder input (joystick ail/elv/rud)
elev, yoke1	The user’s elevator input, as a ratio to full upward deflection. For instance, a value of –1.000 indicated the user is commanding the aircraft’s nose down as fast as possible.
ailrn, yoke1	The user’s aileron input, as a ratio to full rightward deflection. For instance, a value of –1.000 indicated the user is commanding the aircraft to roll left as fast as possible.
ruddr, yoke1	The user’s rudder input, as a ratio to full rightward deflection. For instance, a value of –1.000 indicated the user is commanding the aircraft to yaw left as fast as possible.
Other flight controls
vect, rqst	The requested thrust vectoring.
sweep, rqst	The requested wing sweep.
incid, rqst	The requested wing incidence.
dihed, rqst	The requested wing dihedral.
retra, rqst	The requested wing retraction.
water, jetts	Water jettisoned.
Artificial stability inputs for aileron, elevator, and rudder (art stab ail/elv/rud)
elev, astab	The artificial stability system’s elevator input, as a ratio to full upward deflection.
ailrn, astab	The artificial stability system’s aileron input, as a ratio to full rightward deflection.
ruddr, astab	The artificial stability system’s aileron input, as a ratio to full rightward deflection.
Flight control deflections for aileron, elevator, and rudder (flight con ail/elv/rud)
elev, surf	The proportion of the elevator deflected for upward pitch. If the elevators and flight inputs are in sync, this will match the combined yoke and artificial stability system input.
ailrn, surf	The proportion of the aileron deflected for rightward roll. If the elevators and flight inputs are in sync, this will match the combined yoke and artificial stability system input.
ruddr, surf	The proportion of the rudder deflected for rightward yaw. If the elevators and flight inputs are in sync, this will match the combined yoke and artificial stability system input.
nwhel, steer	The nosewheel’s direction, in degrees of deviation from pointing straight ahead. For instance, a value of –31.000 indicated the wheel is pointed left 31 degrees.
Wing sweep and thrust vectoring (wing sweep/thrust vect)
sweep, 1, deg	The craft’s wing sweep, in degrees back from normal.
sweep, 2, deg	The craft’s wing sweep, in degrees back from normal.
sweep, h, deg	The craft’s wing sweep, in degrees.
vect, ratio	•
sweep, ratio	The craft’s wing sweep, as a ratio to fully forward.
incid, ratio	The craft’s wing incidence, as a ratio to fully angled.
dihed, ratio	The craft’s wing dihedral, as a ratio to fully angled.
retra, ratio	The craft’s wing retraction, as a ratio to fully retracted.
Trim, flaps, slats, and speedbrakes (trim/flap/slat/s-brakes)
trim, elev	Elevator trim.
trim, ailrn	Aileron trim.
trim, ruddr	Rudder trim.
flap, handl	•
flap, postn	Flap position.
slat, ratio	Slat position.
sbrak, handl
sbrak, postn	Speedbrake position.
Landing gear and brakes (gear/brakes)
gear, 0/1	Gear extended status.
wbrak, part	•
lbrak, part	Left toe brake depression.
rbrak, part	Right toe brake depression.
Angular moments
M, ftlb	The aircraft’s total mass.
L, ftlb	The aircraft’s total angular momentum, including all forces (when all is working as it should).
N, ftlb	•
Angular velocities
Q, rad/s	Pitch rate, measured in body-axes (when all is working as it should).
P, rad/s	Roll rate, measured in body-axes (when all is working as it should).
R, rad/s	Yaw rate, measured in body-axes (when all is working as it should).
Pitch, roll, headings
pitch, deg	The aircraft’s pitch, measured in body-axis Euler angles.
roll, deg	The aircraft’s roll, measured in body-axis Euler angles.
hding, true	The aircraft’s true heading, measured in body-axis Euler angles.
hding, mag	The aircraft’s magnetic heading, in degrees.
Angle of attack, sideslip, and paths (AoA, side-slip, paths)
alpha, deg	The aircraft’s angle of attack, in degrees.
beta, deg	The aircraft’s angle of sideslip, in degrees.
hpath, deg	•
vpath, deg	•
slip, deg	•
Magnetic compass (mag compass)
mag, comp	•
mavar, deg	•
Latitude, longitude, and altitude (lat, lon, altitude)
lat, deg	The aircraft’s latitudinal location, in degrees.
lon, deg	The aircraft’s longitudinal location, in degrees.
alt, ftmsl	The aircraft’s altitude, in feet above mean sea level.
alt, ftagl	The aircraft’s altitude, in feet above ground level.
on, runwy	•
alt, ind	•
lat, south	•
lon, west	•
Location, velocity, and distance traveled (loc, vel, dist traveled)
X, m	Relative to the inertial axes.
Y, m	Relative to the inertial axes.
Z, m	Relative to the inertial axes.
vX, m/s	Relative to the inertial axes.
vY, m/s	Relative to the inertial axes.
vZ, m/s	Relative to the inertial axes.
dist, ft	•
dist, nm	•
Latitude for all aircraft (all planes: lat)
lat n, deg	Aircraft n’s latitudinal location (zero if craft n does not exist).
Longitude for all aircraft (all planes: lon)
lon n, deg	Aircraft n’s longitudinal location (zero if craft n does not exist).
Altitude for all aircraft (all planes: alt)
alt n, ftmsl	Aircraft n’s altitude location (zero if craft n does not exist).
Commanded throttle (throttle command)
thron, part	Aircraft n’s commanded throttle.
Actual throttle (throttle actual)
thron, part	Aircraft n’s actual throttle.
Engine or propeller mode (feather-norm-beta-revers)
moden, 0123	Engine n’s current “mode,” where 0 corresponds to feathered, 1 corresponds to normal, 2 to beta, and 3 to reverse thrust.
Propeller setting (prop setting)
propn, set	Aircraft n’s propeller setting.
Mixture setting
mixtn, ratio	Aircraft n’s mixture setting.
Carburetor heat setting (carb heat setting)
heatn, ratio	Aircraft n’s carburetor heat setting.
Cowl flap setting
cowln, set	Aircraft n’s cowl flap setting.
Magneto settings
magnn, set	Aircraft n’s magneto setting.
Starter timeout
starn, sec	Aircraft n’s starter timeout.
Engine power
power, n, hp	Engine n’s power, in horsepower.
Engine thrust
thrst, n, lb	The thrust, in pounds, generated by engine n.
Engine torque
trq n, ftlb	The torque, in foot-pounds, generated by engine n.
Engine RPM
rpm n, engin	The current RPM of engine n.
Propeller RPM (prop RPM)
rpm n, prop	The current RPM of propeller n.
Propeller pitch (prop pitch)
ptchn, deg	The current pitch of propeller n.
Slipstream/propwash/jetwash (propwash/jetwash)
pwash, kt	•
N1
N1 n, pcnt	The current N1 for engine n.
N2
N2 n, pcnt	The current N2 for engine n.
Manifold pressure (MP)
MP n, inhg	The current manifold pressure for engine n, in inches mercury.
Engine pressure ratio (EPR)
EPR n, part	The current engine pressure ratio for engine n.
Fuel flow (FF)
FF n, lb/h	The current fuel flow for engine n, in pounds per hour.
Interstage turbine temperature (ITT)
ITT n, deg	The current interstage turbine temperature for engine n.
Exhaust gas temperature (EGT)
EGT n, deg	The current exhaust gas temperature for engine n.
Cylinder head temperature (CHT)
CHT n, deg	The current cylinder head temperature for engine n.
Oil pressure
OILPn, psi	The current oil pressure for engine n, in pounds per square inch.
Oil temperature (Oil temp)
OILTn, deg	The current oil temperature for engine n.
Fuel pressure
FUEPn, psi	The current fuel pressure for engine n, in pounds per square inch.
Generator amperage
genrn, amp	The current generator amperage for generator n.
Battery amperage
battn, amp	The current batter amperage for battery n.
Battery voltage
battn, volt	The current battery voltage for battery n.
Fuel pump on/off
pumpn, 0/1	Fuel pump n’s status.
Idle speed lo/hi
idlen 0/1	Engine n’s idle speed.
Battery on/off
battn, 0/1	Battery n’s status.
Generator on/off
genrn, 0/1	Generator n’s status.
Inverter on/off
invrn, 0/1	Inverter n’s status.
FADEC on/off
fadec, 0/1	The FADEC’s status.
Igniter on/off
ignin, 0/1	Igniter n’s status.
Fuel weights
fuel, n lb	Fuel tank n’s weight, in pounds.
Payload weights and center of gravity (payload weights and CG)
empty, lb	The aircraft’s empty weight, in pounds.
payld, lb	The aircraft’s payload weight, in pounds.
fuel, totlb	The total weight of the aircraft’s fuel, in pounds.
jetti, lb	The aircraft’s jettisonable weight, in pounds.
curnt, lb	The aircraft’s current weight, in pounds.
maxim, lb	The aircraft’s maximum weight, in pounds.
cg, ftref	The aircraft’s center of gravity, measured in feet behind the reference point.
Aerodynamic forces, in wind axes (aero forces)
lift, lb	The lift acting on the aircraft, in pounds.
drag, lb	The drag acting on the aircraft, in pounds.
side, lb	The side forces acting on the aircraft, in pounds.
Engine forces
norml, lb	•
axial, lb	•
side, lb	•
Landing gear vertical force (landing gear vert force)
gear, lb	•
Landing gear deployment
gear, rat	•
Lift-to-drag ratio and coefficients (lift over drag coeffs)
L/D, ratio	The aircraft’s lift-to-drag ratio.
cl, total	•
cd, total	•
L/D, *etaP	•
Propeller efficiency (prop efficiency)
Peffn, ratio	Propeller n’s efficiency ratio.
Aileron deflections (defs: ailerons)
Lailn,n,deg	The deflection of left aileron n, in degrees.
Railn, n, deg	The deflection of right aileron n, in degrees.
Roll spoiler deflection (defs: roll spoilers)
Lsplr,n, deg	The deflection of left spoiler n, in degrees.
Rsplr, n, deg	The deflection of right spoiler n, in degrees.
Elevator deflections (defs: elevators)
elevn, deg	The deflection of elevator n, in degrees.
Rudder deflection (defs: rudders)
rudrn, deg	The deflection of rudder n, in degrees.
Yaw brake deflections (defs: yaw brakes)
Lyawb, deg	The deflection of the left yaw brake, in degrees.
Ryawb, deg	The deflection of the right yaw brake, in degrees.
Control forces
pitch, lb	The pitch forces acting on the controls in the pilot’s hands.
roll, lb	The roll forces acting on the controls in the pilot’s hands.
hdng, lb	The heading forces acting on the controls in the pilot’s hands.
l-brk, lb	The left brake forces acting on the controls at the pilot’s feet.
r-brk, lb	The right brake forces acting on the controls at the pilot’s feet.
Total vertical thrust vectors (total vert thrust vects)
vertn, tvect	•
Total lateral thrust vectors (total lat thrust vects)
latrn, tvect	•
Pitch cyclic disc tilts
pitch, cycli	•
Roll cyclic disc tilts
roll, cycli	•
Pitch cyclic flapping
pitch, flap
Roll cyclic flapping
roll, flap
Ground effect (lift) from wings (grnd effect lift, wings)
wingn, L cl*
wingn, R cl*	•
Ground effect (drag) from wings (grnd effect drag, wings)
wingn, Lcdi*	•
wingn, Rcdi*	•
Ground effect (wash) from wings (grnd effect wash, wings)
wingn, wash*	•
Ground effect (lift) from stabilizers (grnd effect lift, stabs)
hstab, L cl*	•
hstab, R cl*	•
vstb1, cl*	•
Ground effect (drag) from stabilizers (grnd effect drag, stabs)
hstab, Lcdi*	•
hstab, Rcdi*	•
vstbn, cdi*	•
Ground effect (wash) from stabilizers (grnd effect wash, stabs)
hstab, wash*	•
vstbn, wash*	•
Ground effect (lift) from propellers (grnd effect lift, props)
propn, cl*
Ground effect (drag) from propellers (grnd effect drag, props)
propn, cdi*
Wing lift
wingn, lift	The lift generated by wing n.
Wing drag
wingn, drag	The drag generated by wing n.
Stabilizer lift (stab lift)
hstab, lift	The lift generated by the horizontal stabilizer.
vstbn, lift	The lift generated by the vertical stabilizer.
Stabilizer drag (stab drag)
hstab, drag	The drag generated by the horizontal stabilizer.
vstbn, drag	The drag generated by the vertical stabilizer.
COM 1/2 frequency
COM n, freq	The current frequency of the COM n radio.
COM n, stby	The standby frequency of the COM n radio.
COM, xmt	The transmit status of the COM n.
NAV 1/2 frequency
NAV n, freq	The current frequency of the NAV n radio.
NAV n, stby	The standby frequency of the NAV n radio.
NAV n, type	•
NAV 1/2 OBS
NAV n, OBS	•
NAV n, s-crs	•
NAV n, flag	•
NAV n deflections
NAV n, n-typ	•
NAV n, to-fr	•
NAV n, m-crs	•
NAV n, r-brg	•
NAV n, dme-d	•
NAV n, h-def	•
NAV n, v-def	•
ADF 1/2 status
ADF n, freq	•
ADF n, card	•
ADF n, r-brg	•
ADF n, n-typ	•
DME status
DME, nav01	•
DME, mode	•
DME, found	•
DME, dist	•
DME, speed	•
DME, time	•
DME, n-typ	•
DME–3, freq	•
GPS status
GPS, mode	•
GPS, index	•
dist, nm	•
OBS, mag	•
crs, mag	•
rel, brng	•
hdef, dots	•
vdef, dots	•
Transponder status (XPNDR status)
trans, mode	•
trans, sett	•
trans, ID	•
trans, inter	•
Marker status
OM, morse	Signal from outer marker (OM)
MM, morse	Signal from middle marker (MM)
IM, morse	Signal from inner marker (IM)
audio, activ	•
Switches 1: electrical
avio, 0/1	The status of the AVIO switch.
nav, lite	The status of the navigation light switch.
beacn, lite	The status of the beacon switch.
strob, lite	The status of the strobe light switch.
land, lite	The status of the landing light switch.
taxi, lite	The status of the taxi light switch.
Switches 2: EFIS
ECAM, mode	The ECAM mode.
EFIS, sel n	•
HSI, sel n	•
HSI, arc	•
map, r-sel	•
map, range	•
Switches 3: Autopilot, flight director, and head-up display (switches 3: AP/f-dir/HUD)
ap, src	•
fdir, mode	•
fdir, ptch	•
fdir, roll	•
HUD, power	•
HUD, brite	•
Switches 4: anti-ice
deice, all	•
deice, inlet	•
deice, prop	•
deice, windo	•
deice-n, pitot	•
deice, AOA	•
deice, wing	•
Switches 5: anti-ice/fuel
alt, airn	•
auto, ignit	•
manul, ignit	•
l-eng, tank	•
r-eng, tank	•
Switches 6: clutch and artificial stability (switches 6: clutch/astab)
prero, engag	•
clutc, ratio	•
art, ptch	•
art, roll	•
yaw, damp	•
auto, brake	•
Switches 7: miscellaneous (switches 7: misc)
tot, energ	•
radal, feet	•
prop, sync	•
fethr, mode	•
puffr, power	•
water, scoop	•
arrst, hook	•
chute, deply	•
Annunciators: general
mast, cau	•
mast, war	•
mast, accp	•
auto, disco	•
low, vacum	•
low, volt	•
fuel, quant	•
hyd, press	•
Annunciators: general
yawda, on	•
sbrk, on	•
GPWS, warn	•
ice, warn	•
pitot, off	•
cabin, althi	•
afthr, arm	•
ospd, time	•
Annunciators: engine
fuel, press	•
oil, press	•
oil, temp	•
inver, warn	•
gener, warn	•
chip, detec	•
engin, fire	•
ignit, 0/1	•
Armed autopilot functions (autopilot arms)
nav, arm	•
alt, arm	•
app, arm	•
vnav, enab	•
vnav, arm	•
vnav, time	•
gp, enabl	•
app, typ	•
Autopilot modes
auto, throt	•
mode, hding	•
mode, alt	•
bac, 0/1	•
app,	•
sync, butn	•
Autopilot values
set, speed	The desired speed setting for the autopilot.
set, hding	The desired heading setting for the autopilot.
set, vvi	The desired vertical velocity setting for the autopilot.
dial, alt	•
vnav, alt	•
use, alt	•
sync, roll	•
sync, pitch	•
Weapon status
hdng, delta	•
pitch, delta	•
R, d/sec	•
Q, d/sec	•
rudd, ratio	•
elev, ratio	•
V, kts	•
dis, ft	•
Pressurization status
alt, set	•
vvi, set	•
alt, act	•
vvi, act	•
test, time	•
diff, psi	•
dump, all	•
bleed, src	•
Auxiliary power unit and ground power unit status (APU/GPU status)
APU, eqipd	•
APU, swtch	•
APU, runng	•
APU, N1	•
APU, genrt	•
GPU, power	•
Radar status
targ, selct	The status of the target selection.
Hydraulic status
hydr, pumpn	The status of hydraulic pump n.
hydr, qtyn	The hydraulic fluid in pump n.
hydr, presn	The pressure of hydraulic pump n.
Electrical and solar power status (elec & solar status)
busn, amp	Bus n’s amperage.
busn, volt	Bus n’s voltage.
engin, in W	•
solar, out W	•
batt, w-hr	•
Cross, tie	•
Icing status 1
inlet, ice	•
prop, ice	•
pitot, ice	•
statc, ice	•
Icing status 2
aoa, ice	•
lwing, ice	•
rwing, ice	•
windo, ice	•
Warning status
warn, time	•
caut, time	•
warn, work	•
caut, work	•
gear, work	•
gear, warn	•
stall, warn	•
VRS, ratio	•
Flight plan legs (flite-plan legs)
leg, #	•
leg, type	•
leg, lat	•
leg, lon	•
Hardware options
pedal, nobrk	•
pedal, wibrk	•
yoke, PFC	•
pedal, PFC	•
throt, PFC	•
cecon, PFC	•
switc, PFC	•
btogg, PFC	•
Camera location
camra, lon	The camera’s longitudinal location.
camra, lat	The camera’s latitudinal location.
camra, ele	The camera’s elevation.
camra, hdg	The camera’s heading.
camra, pitch	The camera’s pitch.
camra, roll	The camera’s roll.
camra, clou	The camera’s cloud cover.
Ground location
cntr, X	•
cntr, Y	•
cntr, Z	•
slope, X	•
slope, Z	•
Climb statistics (climb stats)
h-spd, kt	•
v-spd, fpm	•
mult, VxVVI	•
Cruise statistics (cruise stats)
ff, pph	•
ff, gph	•
speed, mph	•
eta, smpg	•
eta, nm/lb	•
range, sm	•
endur, hours	•
mult, VxMPG	•