Python HW Link

High Level Overview

As Flight Simulators increasingly offer support for API interfaces (eg DCS, P3D), it now is feasible to move away from using Joystick interfaces (along with fun of dealing with USB issues) to a distributed system using Ethernet. Such as approach also simplifies output interfacing (e.g. indicators and gauges) as tasks and processes can be divided up across a number of devices and technologies.

This project builds on the Python/Raspberry Pi project used in the Huey Warning panel.

Definitions

Primary Flight Simulator – the PC running an instance of the flight simulator
Primary Node – the Raspberry Pi node that communicates to the Primary Flight Simulator
Distributed Node – either a Raspberry Pi or Arduino (with Ethernet shield) that communicates to the Primary node.

Principles
- Use UDP for all communications where possible. This removes any possible performance issues associated with Nagle and TCP slow start. It also means components are loosely coupled, enabling them to be restarted without impacted other modules.
- Accept inputs from push, toggle, rotary, and rotary encoders.
- Outputs – analog and digital, text. All outputs are normalised before being send to output card/block. Should consider the format used by DCS-BIOS
- Multiple Sim support. As outputs are normalised the and loosely coupled now simulator support can be added without negatively impacting existing sim support. The receive interface from the Sim listens on unique ports, allowing the code to be running at all times.
- A shallow native shim is used to link the simulator to this hardware modules. As an example, LUA is used with DCS, for P3D Sim Connect used.
- Remote shutdown of all Pi nodes is provided through the master, once this has been invoked the nodes will shut down the OS, requiring either a hardware reset, and a power cycle to resume. Ideally outputs will display a checkerboard to reflect a shutdown command has been received.
- Indicator test, a single command will be supported to light all indicators, and perhaps cycle gauges.
- Downstream nodes should accept a request to report input switch position. On receipt of such a request the node will send a report of switch positions, probably at a rate of 20 per second. Need to consider reporting toggle switches in off position and three position switches.
- Will initially develop using DCS, and the variable names currently used by the A10
- The IP addressing of the ‘internal’ network (i.e. between the primary Flight Simulator computer) as well as between nodes will use the 172.16.1.X network. This enabled multiple flight simulators to share a common 192.168.X.X network. If there is only a single simulator the 172.16.1.X network can exist as a secondary address on the Primary network interface, if multiple Simulators share a network, then the internal network should use a different network interface on the Primary Computer.
- Mapping of physical inputs to simulator functions is performed on the Primary Pi node. This keeps the distributed nodes independent of flight sim, and relatively simple, enabling the use Arduino nodes as needed without adding unneeded complexity.
- Each distributed node will have a Unique identifier, which largely is used to uniquely identify different input modules.
- Each distributed node will maintain a state machine for its interfaces, sending only deltas to the Primary Node
- Distributed nodes receiving non-string values receive data as A=V:A1=V1:A2=V2
- Packets from input nodes will have the format of DX:A=V:A1=V1, where X is the input node number. The Node number is only indicated in the front of the packet, not at the individual AV pair.
- If an AV pair is not known it will be silently discarded unless the Primary node is in learning mode – where it will ask the operator what task should be assigned to the unknown AV pair.
- Learning Mode is determined by an argument on the command line ‘learning’ or in the
- Debug Mode is determined by an argument on the command line ‘debug’

Choice of platform for the hardware interface.

Whilst the Raspberry Pi offers the nicest development and troubleshooting environment, it lacks the high pincount found on an Arduino. The Arduino will require an Ethernet shield (and not all Ethernet shields are created equal, have run into issues with an IOT shield that had a poorly cooled chip which caused lock ups).

As the Arduino codes runs without an intermediate operating system, it offers the highest performance for IO related tasks such as driving stepper motors.

Have ran into issues with lockups in the 737 overhead display, possibly due to incorrectly terminated strings or invalid characters included in string. Strongly bounds checking will be performed on the Pi before strings are send to Arduino displays.

As we are not bound by the 128 input limit associated with either windows DirectX or the 32 input limit associated with FSUIPC, OverPro’s Arduino Joystick interface can be used with 256 inputs reducing the number of controllers needed for the pit. Hopefully a single controller for Port, Starboard and Forward zones can be used. OverPro’s code will be modified removing the usb interface, instead storing switch state and reporting deltas after completing a full scan of 256 inputs. Unsure if rotaries will be supported, no logical reason why not.

Program tasks

The workload is divided into two programs – one dealing with inputs, the other with outputs. Both are fundamentally loops which briefly block awaiting receipt of a UDP packet either from the simulator/shim or from the input devices.

Command line parameters are used to get a debugging level as well as enable a configuration mode.

Configurations will be held in two separate files, the format of these files is yet to be determined, but JSON is mostly likely. The configuration files include:
1. IP Address code listens on (optional - if not explicitly configured 127.0.0.1)
2. Port Code listens on (optional – if not explicitly configured 7784 for input module and 7785 for output module. (still considering whether to leave export.lua sending direct to existing Arduino units)
3. Mapping of input to aircraft commands and aircraft outputs to physical displays/gauges.

Protocols

Where possibly output values will be carried directly mapping to value to be displayed, and may be integer, float, or string. Indicators/Solenoids will be represented as a 0 or 1.

Data will be carried as AV pairs A1:V2, A2:V2. The data packet will be preceded with a D.

Operational tasks such as shutdown, reboot, refresh switch state will be preceded with a C (command), and a single operational task. Eg C9999.

Operational Task

Task Id	Task

CQ	Send all switch states

Ikarus uses the following format

# If Sending Commands to DCS with Ikarus installed
# The values to be sent can be found
# C:\Program Files\Eagle Dynamics\DCS World\Mods\aircraft\Uh-1H\Input\UH-1H\joystick
# Structure is
# C - Command
# 15 - Cockpit Device Id
# 3003 - Unknown but seen in multiple places
# Switch Position
# Send to Port UDP_PORT = 26027
# MESSAGE = "C15,3003,-1" - Turns Test Switch on - All warning lights
# MESSAGE = "C15,3003,0" - Turns Test Switch to centre
# MESSAGE = "C15,3003,1" - Turns Test Switch to Reset - clears caution on front panel
# Bright/Dim 15,3004

Learnings from Different Modules
USB Interfaces

There still is a need to use USB interfaces, such as for a High Resolution Analog interface (which already has noise reduction built in) or for Rotary Encoders. As the Leo Bodnar cards provide a solid rotary interface they will be used for inputs on radios and autopilots.

The follow vendor and product Ids are used for the Leo Bodnar cards:

	Vendor Id	Product Id
BU0836	0x16c0	0x05b5
BU0836X	0x1dd2	0x1001
BBI-32	tba	tba

The USB interfaces will still be normalised over the UDP interfaces, and should support requests to report the status of all Joystick interfaces, perhaps with a 10mS delay between the sending the status of each button input.

It appears that different Operating Systems provide different levels of accessiblity, epsecially around devices they are Human Interfaces (HIDs). The Mac won’t let you easily attach to the HID. This isn’t too much of an issue, but does mean testing needs to be done on the Pi itself.

Raspberry Pi
The USB.Core library provides a low level interface for the Rapsberry Pi. It is able to scan the USB bus and report back what is attached.
The code scans the USB bus looking for a specific device, and then detaches the device from the Kernel driver. Once this is completes it then runs a set configuration, and then asks for a data block from the target device on a frequent interval.
A quick check is made to see if the value returned is different from the last interval, if it is then the list holding switch positions if refreshed

Initiating Scripts on Pi Nodes

Instead of trying to start python directly from crontab, use shell script (usually my_server) to
start things

To get the script to autostart
sudo crontab -e

And add line
@reboot sh /home/pi/Documents/Flightsim/Huey\ Caution\ Panel/my_server 2>&1

Which results in the crontab file looking like

# Edit this file to introduce tasks to be run by cron.
..
..
#
@reboot sh /home/pi/Documents/Flightsim/Huey\ Caution\ Panel/my_server 2>&1

Originally a separate shutdown script was operated, need to work out why it was commented out, possibly as the script below only ever reaches remoteshut.py after the receiver code exits, which is never…

### BEGIN INIT INFO
# Provides: my_server
# Required-Start: $remote_fs $syslog $network
# Required-Stop: $remote_fs $syslog $network
# Default-Start: 2 3 4 5
# Default-Stop: 0 1 6
# Short-Description: Simple Web Server
# Description: Simple Web Server
### END INIT INFO

#! /bin/sh
# /etc/init.d/my_server

export HOME
echo "Starting My Server"
cd /home/pi/Documents/Flightsim/Huey\ Caution\ Panel
sudo /usr/bin/python receiver_004.py 2>&1 &
#sudo /usr/bin/python remoteshut.py 2>&1 &
exit 0
Receive UDP Port utilisation

A number of these values are referenced from soic_conv_ExportStart.lua from DCS

Port	IP Address	Description

26027	127.0.0.1	DCS_Emulator_Rx
	127.0.0.1	New DCS Emulator
7777	127.0.0.1	SOIC on Primary Sim PC[1]
7784		Input Codes listens on

7788	127.0.0.1	Arduino Sendor Emulator. Sends to DCS_Emulator RX

13135	192.168.1.105	Fuel Hands on A10
13135	192.168.1.106	Fuel Display (OLED on A10)
13135	192.168.1.107	Compass and Clock Analog hands
13135	192.168.1.108	Clock Digits
13135	192.168.1.109	General Stepper

Adding RS232 Interface

Ref - https://www.instructables.com/id/Read-and-write-from-serial-port-with-Raspberry-Pi/

Using Max 3232 based interface which supports 3.3 to 5V
Pin Used (remebering pin numbers does include both sides of header – so these pins are adjacent.
4 (5V),
6 (GND)
8 (TX),
10 (RX)

Can use sudo raspi-config → Interfacing Options → Serial to enable/disable console through serial interface. In the disti used in Dec 2018 it is disabled by default – enabled to validate the TX led flashes during the reload process.

Notes from the Huey readme
 The SOIC port points to another Shim which maintains a TCP connection to the SOIC processes, converting the UDP payload into a TCP stream. Currently error handling does not address a restart of SOIC processes.

Git Commands

Clone Repo
git clone https://github.com/bnepethomas/bne-arduino-flight-simulator-interfaces.git

git config --global user.email "your email”
git config user.name "your name"

Watch for untracked files

$ git add .
$ git commit .
$ git push

Code Modules

UDP_Reflector

Displays and optionally forwards packets to a wireshark receiver
Listens on a well known port 27000 (ie fixed)
By default displays all packets but will filter using simple character matching (no wild carding)

Command line options
a: filterstring - display packets containing this string
b: IP Address and Port to send to wireshark
PhyHWLink_Pri_Node_Input

Code Status

	Complete	Cmd_line	Debug	Config_File	Doc
UDP_Reflector

Coding Learnings

Logging

The logging module (import logging) enable you to determine which messages will be displayed on the console

logging.basicConfig(format='%(asctime)s:%(levelname)s:%(message)s',level=logging.INFO)
#logging.basicConfig(format='%(asctime)s:%(levelname)s:%(message)s',level=logging.DEBUG)

Once the value is set it cannot be changed mid-execution, so it is best to set at the top of the program.

Command Line Parameters

Command line parameters (from optparse import OptionParser) are easily managed with this module.

D:\>UDP_Reflector.py --help
2019-01-13 07:49:41,712:INFO:Unable to find UDP_Reflector_config.py
Usage: UDP_Reflector.py [options]

Options:
  -h, --help show this help message and exit
  -w opt_W_Host, --wh=opt_W_Host
        Wireshark Target IP Address
  -u opt_W_Port, --wp=opt_W_Port
        Wireshark Target Port. 27001 is used if not explicity
        specified

Command line options are easily added, including help.

parser = OptionParser()

parser.add_option("-w","--wh", dest="opt_W_Host",
help="Wireshark Target IP Address",metavar="opt_W_Host")
parser.add_option("-u","--wp", dest="opt_W_Port",
help="Wireshark Target Port. 27001 is used if not explicitly specified",
      metavar="opt_W_Port")

(options, args) = parser.parse_args()

logging.debug("options:" + str(options))
logging.debug("arguments:" + str(args))

if options.opt_W_Host != None:
wireshark_IP_Address = str(options.opt_W_Host)

if options.opt_W_Port != None:
wireshark_Port = str(options.opt_W_Port)

if wireshark_IP_Address != None:
logging.info("Wireshark host is : " + wireshark_IP_Address)
logging.info("Wireshark UDP port is : " + str(wireshark_Port))

if len(args) != 0:
filterString = args[0]
logging.info("Display Filter is :" + str(args[0]))

Configuration Files

A local file can hold settings for a program. Its a good idea to simple extend the name of the primary code with ‘_config’ at the end. The file type should be ‘.py’

e.g. PyHWLink_UDP_Reflector configuration file is UDP_Reflector_config.py

The values are loaded early in the code

try:

    if not (os.path.isfile(config_file)):

        logging.info('Unable to find ' + config_file)

    else:
        try:
        from config_file import *

        except Exception as other:
        logging.critical("Error in Initialisation: " + str(other))

        print('Unable to open "' + config_file + '"' )
        print('Or variable assignment incorrect - forgot quotes for string?')
        print('Defaults used')

The configuration file looks like a series of variable assignments

learning = True
AircraftType = 'A10C'

Error Handling In Python

Its good form to use the try and except constructs,
Of note in this code, is a workaround to avoid the use of threads. As the code has a single purposed of receiving a workload and then processing it, blocking isn’t a big issue. However it is good form to provide some updates to the user
def ReceivePacket():

    while True:

        try:

        data, (Source_IP, Source_Port) = serverSock.recvfrom(1500)

        ReceivedPacket = data
        packets_processed = packets_processed + 1

        ProcessReceivedString( str(ReceivedPacket), Source_IP , str(Source_Port) )

        logging.debug("Iterations since last packet " + str(iterations_Since_Last_Packet))

        except socket.timeout:
        iterations_Since_Last_Packet = iterations_Since_Last_Packet + 1
        if debugging == True and (iterations_Since_Last_Packet > 10000):
        print("[i] Mid Receive Timeout - " + time.asctime())
        iterations_Since_Last_Packet=0

        last_time_display = time.time()
        packets_processed = 0
        continue

        except Exception as other:
        logging.critical('Error in ReceivePacket: ' + str(other))

2019-01-13 08:25:39,410:INFO:Unable to find UDP_Reflector_config.py
Listening on port 27000
2019-01-13 08:25:44,424:INFO:Keepalive check 0 Packets Processed. 0 packets per second.
2019-01-13 08:25:49,438:INFO:Keepalive check 0 Packets Processed. 0 packets per second.

Having a catch-all exception handler ensures that something is logged if an exception occurs. Included in excepted captures should be a Ctrl-C to gracefully exit, cleaning up resources.

def CleanUpAndExit():
    try:
        # Catch Ctl-C and quit
        print('')
        print('Exiting')
        print('')
        try:
        serverSock.close()
        except:
        logging.critical('Unable to close server socket')
        sys.exit(0)

    except Exception as other:
        logging.critical('Error in CleanUpAndExit: ' + str(other))
        sys.exit(0)

def Main():

    print('Listening on port ' + str(UDP_Port))
    try:

        ReceivePacket()

    except KeyboardInterrupt:
        # Catch Ctl-C and quit
        CleanUpAndExit()

    except Exception as other:
        logging.critical('Error in Main: ' + str(other))

Main()

PI Addressing

The Pi Ethernet interface has been configured with a secondary interface. This doesn’t seem possible using dhcpd.conf - so using /etc/network/interfaces. Using the Wireless interface to assign a default route and DNS server.

Currently unable to SSH to 144 but can 145 (wired). Also if a ping is made to wired interface - the reply originates with Mac address of wireless

auto lo
iface lo inet loopback
auto eth0
allow-hotplug eth0
iface eth0 inet static
       address 192.168.1.145
       netmask 255.255.255.0
auto eth0:1
iface eth0:1 inet static
       address 192.168.3.100
       netmask 255.255.255.0
auto wlan0
allow-hotplug wlan0
iface wlan0 inet dhcp
wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf