Hornet Pit Assembly and Disassembly

# Disassembly
## Remove Seat
### Disconnect Cable
### Remove Rear Support Cross Member
### Remove Seat Base Screws
Slide Seat Slightly back
### Remove Stick USB cable
### Lower seat rollers
### Slide Seat out

## Remove Skins and UIP Cover
Remove bolts for UIP
Disconnect AOA indicator and place in the forward bay. Start from the outside and work inwards, taking care not to scratch paint as the skin lifts.

Remove the alignment plates

## Remove Canopy Bow
Disconnect cables from the LED distribution board
Disconnect the Map Light cable from the PWM light distribution panel in the UIP
Disconnect the Compass cables
Unscrew the Canopy bow itself
Remove the canopy bow support brackets
## UIP
### Power Distribution Panel
## Disconnect Port/Left Console
Note there are nuts located midway along the bolt (between the console and UIP) that hold the bolt in place.

## Disconnect Cables
USB	Bone	Bone
Port Side PWM	Black	Green
Left console Flood left console
12V	Black	Red
Left Console Stepper Servos	White	Yellow
Left Console Digital Out	White	Red
Left Console	Black	Orange

## Disconnect Starboard/Right Console

Note the nuts sitting midway along bolts to hold the bolt in position

### Disconnect Cables
The cables stay attached to the console
Role	Cable Colour	Connector
Ethernet	Blue
Right Conn Power	Black
Strb Side Dimmer	Black	4 way Green
UFC Analog	White
Right Console LIP Servos	Black	6 way Yellow
Right Console LIP Digital	Back	6 way unpainted
Right Console LED	Black?	4 way Orange
Right Console LIP Stepper	Black
Dimmer Pots	Black	Blue
USB	Blue
12V	Black	Red
These could be left console
Something Power (utility light?)	Gray/Black	2 way unpainted
Ethernet	Blue
Backlighting	White	4 way Black
USB	Bone

The Forward Assembly is now standalone