Simulator To Do’s
Hornet

Circuit breakers – Centre two swapped out not working – test using udp monitor
A/A and A/G led not lighting – check flow of Pixel leds in code – probably pixel led failure – await new design
Set all panel backlighting to mid and flood lights to low after power up – updated pixel led
Rudder Trim – harden code and validate it is being received to full extends
Calibrate Stand by airspeed – determine majors and then range – just use model speed as reference
Instrument backlighting on startup

A10
CMSP display not staying in synch
Set flood lights on DCS Pause – determine DCS is paused and turn on flood lights
Check Compass pinouts against Ben’s compass
Stream Deck slow or locked up – test direct PC connectivity
Arduino GPS is it working on the Hornet, if so how
Adjust and set default snap view
Correct Joystick mappings – coolee hat
RWR doesn’t appear to be function – check through BIT test
Dual lines on CMSP display